Job Hazard Analysis and Mitigation Form

Task or Employee:    ATLAS Pixel worker 	 	Routine		Non-routine

For instructions on filling out this form, please see the webpage at http://www-group.slac.stanford.edu/esh/general/hazanalysis/ .  Routine JHAMs are kept by the employee and supervisor. Non-routine JHAMs are kept until the task is fully closed out (however, in case of an incident, the form is to be kept for use by the review team). All participants should sign in the Acknowledgement section on the last page.

| Basic Job Steps | Potential Hazards | Controls & Recommended Actions | Training Associated |
| --- | --- | --- | --- |
| Working on or near opto boards. | Opto boards are made with BeO. If the board is broken and the resulting powder is ingested or inhaled, it can cause chronic beryllium disease and is a carcinogen. | Provide warning signs. Protective cover over opto boards should not be disturbed. Ensure work area is well ventilated. Minimize working time near opto boards. Wash hands after working in the vicinity. | Recognize opto boards. Understand the potential hazards of BeO powder. |
| Attach and detach services. | Trip hazards. The pixel integration area has many temporary service lines during the assembly phase. They present potential trip hazards while they are being moved and laid down. | Erect barriers and signs to warn people and keep them away from hazard areas. Those working within the areas, e.g. to route cables, should pay particular attention to their footing. |  |
| Attach and detach electrical lines. | Electrical hazards. Pixel electronics uses both low-voltage (~5 V), and high-voltage (~100 V) supplies. | High voltage (~100 V) supplies are current limited to few mA. Connectors on supply side have recessed female contacts. |  |
| Working in SR-1 building. | SR-1 is the pixel detector integration area. Exposure to all the work activities: Moving machinery. Slips, trips & falls. Crane hazards. Electrical hazards. | Observe and follow safety regulations and signs. Respect barricades and postings. Do not touch equipment unless you are sure it is OK to do so. Be aware of your surroundings. |  |

(Add rows by placing cursor in the right box of the last row and entering a tab.)

| Acknowledgements |  |  |
| --- | --- | --- |
|  | Print Name | Signature | Date |
| Supervisor: |  |  |  |
| Participants: |  |  |  |