FFTB Tunnel Activities: Monday 10/11/04 Day Shift

J. C. Sheppard 10/11/04 16:23

- Aligned 6100-6130 area beam pipe and BPM. Tube and BPM were raised vertically (up) by about 5 mm. A “good” orbit should zero BPM 6130 position (try YCOR 6100 = - 0.275 kG-m, YCOR 6130 = -0.232 kG-m for starters, zero both BPM 6090 and 6130 with upstream correctors; use YCOR 6100 sparingly for this alignment step)

- new camera lens for FFTB dump screen; larger field of view

- PROF 6100 now has IN/OUT SCP status via a single Out limit switch; reads back on SCP panel

- Aligned PROF 6100 camera to specular reflection from PROF 6100 screen

- Moved PC7.6 and PC 7.7 0.2”” to the south and 0.25” up (both collimators moved the same amount in both planes)

- Checked alignment of BPM 6160; no change

- Added scintillator detectors at end of gamma line and in behind CsI target (PROF 6190)

- Run/Safe switch in Run position for CB02 SOLN 6203, 6204

- No action taken on VP1040, VACG2020

- CB02 TOROs 5100 and 630 are presently not available as machine diagnostics (have been taken over for a BCS toroid comparator).

- No action taken (as far as I know) in regards to looking a the operation of the power supplies for CB02 SLON 6203, 6204. This item can wait until Tuesday day shift

Request for Operations when the machine is turned on:

Reestablish beam in FFTB, steer around alignment change at BPM 6130; minimize beam loss and “noise” on PLIC, LION, PIC,…sundry loss monitors.

Look for gamma beam with PROF 6100 inserted (try YCOR 6100 = - 0.275 kG-m, YCOR 6130 = -0.232 kG-m for starters)

Quad shunt QP6 to look if center of BPM 6130 and QP6 are in agreement

Measure beam sizes at WIRE 6100 and WIRE 6180