| GLAST LAT ACD ELECTRONICS SUBSYSTEM Technical Document | Document # | Date Effective |
| --- | --- | --- |
|  | ACD-PROC-000066 | 12-30-02 |
|  | Prepared by: | Supersedes |
|  | Glenn Unger | None |
| Document Title |
| GLAST LAT ACD PMT Subassembly Test Procedure |

Gamma-ray Large Area Space Telescope (GLAST)

Large Area Telescope (LAT)

Anti-Coincidence Detector (ACD)

PMT Subassembly Test Procedure

DRAFT

Test Equipment Required

- Oscilloscope with the capabilities to store a picture to a 3.5” floppy disk

- High voltage power supply with the ability to monitor current and voltage to a resolution of 1 mA and 10 volts, and a 0 volt to 1500 volt range

##### Test Procedure

- Turn the high voltage supply voltage to 0 volts.

- Power-OFF the high voltage supply.

- Power-ON the oscilloscope.

- Set the oscilloscope Time/Div to 10 nanoseconds.

- Set the oscilloscope, channel xx, Volt/Div to 10 millivolts.

- Set the oscilloscope channel xx signal input termination to 1-megaohm.

- Connect the fiber portion of a tile to the top of PMT subassembly’s housing opening.

- Tape the tile-to_PMT interface and cover the tile with a dark cloth

- Connect the PMT subassembly high voltage cable to the high voltage supply

- Connect the PMT subassembly signal cable to channel xx

- Power-ON the high voltage supply

- Increase the voltage to 100 volts and monitor the current.  The current should fall below 2 microamps within a few seconds.  If it doesn’t, STOP the test and determine the problem.

- Increase the voltage to 200 volts and monitor the current.  The current should fall below 2 microamps within a few seconds.  If it doesn’t, STOP the test and determine the problem.

- Increase the voltage to 500 volts and monitor the current.  The current should fall below 2 microamps within a few seconds.  If it doesn’t, STOP the test and determine the problem.

- Increase the voltage to 800 volts and monitor the current.  The current should fall below 2 microamps.  If it doesn’t, STOP the test and determine the problem.

- Set the trigger level between –10 millivolts and –20 millivolts or until a negative going pulse is acquired on the oscilloscope.

- Save a picture to the floppy disk and include it in the PMT subassembly certification log.

- End of test.