ContriguratorGUI is a trigger configuration tool. It is capable of:

- Configuring (using LATTE4) all GEM registers except external timing, tower busy, parity/plumbing registers

- Creating a “configParser” format file to represent a configuration

- Reading a “configParser” format file to load a configuration

- Creating a csv representation of the scheduler for a given configuration

- The configurations are useable by INT end2end and DataTaking scripts

Limitations, things needing to be done:

- The scheduler is created by allowing each engine to have a precendence, and a “Yes/No/Don’t Care” setting for each bit of the condition summary. This is not the most general way of configuring the scheduler.

- The standalone tool cannot create a register representation of the GEM (needs LATTE4)

- As mentioned above, there are configurable registers that may be wanted (external delay, tower busy, etc.

- ACD tile input enables are not individually configurable (user given option of all or only those tiles in the ROI configuration file)

- Engine precedence is tied to engine number. They should be decoupled by allowing assignation of  priority/number independently.

The remainder of this document consists of:

- ContriguratorGUI screenshots. The GUI is divided into several tabs. These screenshots show the proposed flight trigger configuration for the LAT from the Nov 21 test planning meeting

- The “configParser” file representing the configuration above

- The spreadsheet of the scheduler created by the above configuration

These documents are also available for now at:

- http://www.slac.stanford.edu/~lmiller/trg_flight.cfg

- http://www.slac.stanford.edu/~lmiller/scheduler.csv

This is the .cfg file for the above configuration.

[acd]

roifile = 	veto_shadow

use_acd_as_trigger = 	False

[conditions0]

calhigh = 	None

callow = 	None

cno = 		None

external = 	None

periodic = 	None

roi = 		None

solicited = 	True

tracker = 	None

[conditions1]

calhigh = 	None

callow = 	None

cno = 		None

external = 	None

periodic = 	True

roi = 		None

solicited = 	False

tracker = 	None

[conditions10]

calhigh = 	False

callow = 	False

cno = 		False

external = 	None

periodic = 	None

roi = 		True

solicited = 	False

tracker = 	False

[conditions11]

calhigh = 	False

callow = 	False

cno = 		False

external = 	False

periodic = 	False

roi = 		False

solicited = 	False

tracker = 	False

[conditions12]

calhigh = 	False

callow = 	False

cno = 		False

external = 	True

periodic = 	False

roi = 		False

solicited = 	False

tracker = 	False

[conditions13]

calhigh = 	False

callow = 	False

cno = 		False

external = 	False

periodic = 	False

roi = 		False

solicited = 	False

tracker = 	False

[conditions14]

calhigh = 	None

callow = 	None

cno = 		None

external = 	None

periodic = 	None

roi = 		None

solicited = 	None

tracker = 	None

[conditions15]

calhigh = 	None

callow = 	None

cno = 		None

external = 	None

periodic = 	None

roi = 		None

solicited = 	None

tracker = 	None

[conditions2]

calhigh = 	None

callow = 	None

cno = 		True

external = 	None

periodic = 	None

roi = 		None

solicited = 	False

tracker = 	None

[conditions3]

calhigh = 	True

callow = 	None

cno = 		False

external = 	None

periodic = 	None

roi = 		None

solicited = 	False

tracker = 	None

[conditions4]

calhigh = 	False

callow = 	True

cno = 		False

external = 	None

periodic = 	None

roi = 		False

solicited = 	False

tracker = 	True

[conditions5]

calhigh = 	False

callow = 	True

cno = 		False

external = 	None

periodic = 	None

roi = 		False

solicited = 	False

tracker = 	True

[conditions6]

calhigh = 	False

callow = 	True

cno = 		False

external = 	None

periodic = 	None

roi = 		False

solicited = 	False

tracker = 	False

[conditions7]

calhigh = 	False

callow = 	True

cno = 		False

external = 	None

periodic = 	None

roi = 		True

solicited = 	False

tracker = 	False

[conditions8]

calhigh = 	False

callow = 	False

cno = 		False

external = 	None

periodic = 	None

roi = 		True

solicited = 	False

tracker = 	True

[conditions9]

calhigh = 	False

callow = 	True

cno = 		False

external = 	None

periodic = 	None

roi = 		True

solicited = 	False

tracker = 	True

[engine0]

calstrobe = 	False

fourrange = 	False

inhibit = 	False

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine1]

calstrobe = 	False

fourrange = 	True

inhibit = 	False

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	False

[engine10]

calstrobe = 	False

fourrange = 	False

inhibit = 	True

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine11]

calstrobe = 	False

fourrange = 	False

inhibit = 	True

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine12]

calstrobe = 	False

fourrange = 	False

inhibit = 	True

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine13]

calstrobe = 	False

fourrange = 	False

inhibit = 	False

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine14]

calstrobe = 	False

fourrange = 	False

inhibit = 	True

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine15]

calstrobe = 	False

fourrange = 	False

inhibit = 	False

marker = 	5

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine2]

calstrobe = 	False

fourrange = 	True

inhibit = 	False

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine3]

calstrobe = 	False

fourrange = 	False

inhibit = 	False

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine4]

calstrobe = 	False

fourrange = 	False

inhibit = 	False

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine5]

calstrobe = 	False

fourrange = 	False

inhibit = 	False

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine6]

calstrobe = 	False

fourrange = 	False

inhibit = 	False

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine7]

calstrobe = 	False

fourrange = 	False

inhibit = 	False

marker = 	0

prescale = 	0

tack = 		True

zerosuppress = 	True

[engine8]

calstrobe = 	False

fourrange = 	False

inhibit = 	False

marker = 	0

prescale = 	100

tack = 		True

zerosuppress = 	True

[engine9]

calstrobe = 	False

fourrange = 	False

inhibit = 	False

marker = 	0

prescale = 	100

tack = 		True

zerosuppress = 	True

[input_enables]

calhigh0 = 	True

calhigh1 = 	True

calhigh10 = 	True

calhigh11 = 	True

calhigh12 = 	True

calhigh13 = 	True

calhigh14 = 	True

calhigh15 = 	True

calhigh2 = 	True

calhigh3 = 	True

calhigh4 = 	True

calhigh5 = 	True

calhigh6 = 	True

calhigh7 = 	True

calhigh8 = 	True

calhigh9 = 	True

callow0 = 	True

callow1 = 	True

callow10 = 	True

callow11 = 	True

callow12 = 	True

callow13 = 	True

callow14 = 	True

callow15 = 	True

callow2 = 	True

callow3 = 	True

callow4 = 	True

callow5 = 	True

callow6 = 	True

callow7 = 	True

callow8 = 	True

callow9 = 	True

cno0 = 		True

cno1 = 		True

cno10 = 	True

cno11 = 	True

cno2 = 		True

cno3 = 		True

cno4 = 		True

cno5 = 		True

cno6 = 		True

cno7 = 		True

cno8 = 		True

cno9 = 		True

external = 	False

roi_tile_only = 	False

tkr0 = 		True

tkr1 = 		True

tkr10 = 	True

tkr11 = 	True

tkr12 = 	True

tkr13 = 	True

tkr14 = 	True

tkr15 = 	True

tkr2 = 		True

tkr3 = 		True

tkr4 = 		True

tkr5 = 		True

tkr6 = 		True

tkr7 = 		True

tkr8 = 		True

tkr9 = 		True

[periodic]

periodic_limit = 	-1

periodic_pps = 	True

periodic_prescale = 	10

[window]

calhigh = 	True

callow = 	True

cno = 		True

external = 	False

periodic = 	True

roi = 		False

solicited = 	True

tkr = 		True

width = 	12

Finally, the csv file which represents the scheduler.

| file scheduler.csv created by contriguratorGUIImpl on Mon Nov 21 13:30:25 2005 |  |
| --- | --- |
| Bit number |  |  |  |  |  |  | Engine Number |
| Roi | Tkr | Cal Low | Cal High | CNO | Periodic | Solicited | External |  |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 11 |
| 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10 |
| 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 14 |
| 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 8 |
| 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 6 |
| 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 7 |
| 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 4 |
| 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 9 |
| 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 3 |
| 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 3 |
| 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 3 |
| 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 3 |
| 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 3 |
| 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 3 |
| 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 3 |
| 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 3 |
| 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 2 |
| 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 2 |
| 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 2 |
| 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 2 |
| 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 2 |
| 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 2 |
| 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 2 |
| 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 2 |
| 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 2 |
| 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 2 |
| 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 2 |
| 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 2 |
| 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 2 |
| 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 2 |
| 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 2 |
| 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 2 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |
| 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 |
| 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 |
| 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 |
| 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 |
| 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 |
| 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 |
| 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 |
| 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 |
| 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 |
| 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 |
| 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 |
| 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 |
| 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 |
| 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 |
| 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 |
| 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 |
| 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 |
| 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |
| 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |
| 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 |
| 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 |
| 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 |
| 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 |
| 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 |
| 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 |
| 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 |
| 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 |
| 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 |
| 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 |
| 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 |
| 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |
| 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |
| 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |
| 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 |
| 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 |
| 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 |
| 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 |
| 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 |
| 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 |
| 0 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 |
| 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 |
| 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |
| 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |
| 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |
| 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |
| 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 |
| 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 |
| 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 |
| 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 |
| 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 |
| 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 |
| 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 |
| 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 |
| 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 |
| 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 |
| 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 |
| 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 |
| 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 |
| 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 |
| 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 |
| 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 |
| 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0 |
| 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 |
| 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 |
| 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 |
| 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 |
| 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |
| 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |
| 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 12 |
| 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 10 |
| 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 14 |
| 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 8 |
| 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 6 |
| 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 7 |
| 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 4 |
| 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 9 |
| 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 3 |
| 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 3 |
| 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 3 |
| 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 3 |
| 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 3 |
| 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 3 |
| 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 3 |
| 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 3 |
| 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 2 |
| 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 2 |
| 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 2 |
| 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 2 |
| 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 2 |
| 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 2 |
| 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 2 |
| 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 2 |
| 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 2 |
| 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 2 |
| 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 2 |
| 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 2 |
| 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 2 |
| 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 2 |
| 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 2 |
| 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 2 |
| 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 |
| 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 |
| 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 |
| 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 |
| 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 |
| 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 |
| 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 |
| 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 |
| 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 |
| 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 |
| 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 |
| 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 |
| 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 |
| 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 |
| 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |
| 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |
| 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |
| 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 |
| 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 |
| 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 |
| 1 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 |
| 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 |
| 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 |
| 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 |
| 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 |
| 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 |
| 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 |
| 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |
| 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |
| 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |
| 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 |
| 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 |
| 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 |
| 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 |
| 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 |
| 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 |
| 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 |
| 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 |
| 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 |
| 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 |
| 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 |
| 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 |
| 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 |
| 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 |
| 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 |
| 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 |
| 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 |
| 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 |
| 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 |
| 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 |
| 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 |
| 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 |
| 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 |
| 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 |
| 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 |
| 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 |
| 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 |
| 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 |
| 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 |
| 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 |
| 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 |
| 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 |
| 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 |
| 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 |
| 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 |
| 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 |
| 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 |
| 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 |
| 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 |
| 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 |
| 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 |
| 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 |
| 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 |
| 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 |
| 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 |
| 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 |
| 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 |
| 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 |
| 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 |
| 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 |
| 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 |