Initial Commissioning Tasks for the LTU/FEL Run (2008-2009)

Oct. 20, 2008

The First Four Weeks (Nov. 3 - 28, 2008)

Main Goal:	Re-establish bright beam to 52-SL2 at 30 Hz & 0.25 nC

- All injector, linac, and BSY pre-beam checkout done and all magnets standardized to startup configs (per R. Iverson)

- No unnecessary new controls software released yet

- RF processing of gun and injector RF (gun separated from L0a/b with VV01)

  - See Axel Brachmann’s procedure (6.0 MV max. gun voltage)

  - Note TCAV0 (20-5) was vented and 21-1 klystron was replaced

- Re-establish UV drive laser on VCC and cathode with 1.2-mm iris and ~20 µJ

  - Run through laser checklist

  - Re-GOLD (if necessary) and switch ON the laser pointing feedback loops

- Take beam to 6-MeV spectrometer (1-10 Hz)

  - Image cathode on YAG01 and verify cathode position (no “spider”)

  - Measure QE

  - Align laser using solenoid-scan GUI (with Aug. ’08 offsets)

  - Steer beam flat in x and y using minimal corrector tweaks

  - Calibrate gun RF amplitude on YAGG1 (6-MeV spectrometer)

  - Re-GOLD (if necessary) and switch ON the following feedback loops:

    - Laser loop

    - Laser Power Set

    - Bunch charge

- Take beam to 135-MeV spectrometer (1-10 Hz, see procedure)

  - New laser-heater chicane OFF, LH-undulator not installed, and no IR laser

  - Phase and calibrate L0a amplitude on YAGS2 (135-MeV spectrometer)

  - Phase and calibrate L0b amplitude on YAGS2 (135-MeV spectrometer)

  - Check YAGS2 for “on-crest” operation (no linear chirp)

  - If time allows, measure OTR2 Twiss & emittance and run β-matching, and correct any induced steering

  - If time allows, measure bunch length on OTR2 with TCAV0

  - Re-GOLD (if necessary) and switch ON injector feedback loops:

    - Gun launch

    - Injector launch

- Take beam to TD11 stopper with BC1 ON at R56 = 45.5 mm, BC1 offset = 247.6 mm, and energy = 250 MeV (1-10 Hz)

  - Adjust L1S voltage roughly to get beam through BC1 (L1X OFF)

  - Steer beam reasonably flat in x and y using minimal corrector tweaks

  - Calibrate L1S amplitude at crest phase using the BC1 BPM (L1X OFF)

  - Re-GOLD and switch ON BC1 energy feedback (with DL1 energy, but no BC1 bunch length yet)

  - Phase L1S OFF crest by 21 degrees (see OP GUI)

  - Calibrate L1X amplitude at decal-crest phase using the BC1 BPM (scan L1X voltage and correlate with L1S voltage feedback response needed to hold BC1 BPM constant in x)

  - Re-GOLD (with BPMS LI21 201 x = +0.1 mm) and switch ON X-cavity launch feedback loop

  - Phase L1X OFF crest by 160 degrees (see OP GUI)

  - Check BL11 mirror is inserted

  - If ready, re-GOLD (if necessary) and switch ON BC1-bunch-length feedback loop (+ DL1-energy + BC1-energy)

- Checkout injector BPM timing, attenuation, and reasonable response to a few oscillations (any BPMs now backwards or not responding in x, y, or TMIT?)

- Take beam to 52-SL2 stopper at 13.64 GeV with BC2 ON at R56 = 24.7 mm, BC2 offset = 363.0 mm, and BC2 energy = 4.3 GeV (1-10 Hz)

  - Standardize LI21 quadrupole and corrector magnets

  - Add or remove klystrons to get beam through BC2

  - Steer beam flat (or to config) in x and y using minimal corrector tweaks

  - Phase all RF stations (21-3 to 30-8, with all SBST PDES = 0)

  - Set L2 RF phase to 36 deg using phase-scan GUI

  - Check BL21 mirror is inserted

  - Re-GOLD (if necessary) and switch ON linac/energy feedback loops:

    - L2 launch

    - LI26 SCP loop

    - DL1-energy, BC1-energy, BC1-bunch-length, BC2-energy, and BC2-bunch-length

    - FB31 energy loop

- Measure and correct emittance at OTR2, WS12, and WS28