During FY 05, the LCLS controls group would like to prototype and verify our critical technologies. During this year, we should purchase, build, or otherwise acquire and evaluate our first examples of hardware solutions that are needed. Equally important in this year is the first steps in the integration of the “SLC-aware” IOC.

We have identified the key hardware elements and prioritized them as follows: First priority - SLC timing into EPICS, EPICS event generator, EPICS event receiver, laser control (motors and standard I/O), beam position monitors,  bunch length monitors, coherent radiation auto correlator, and personnel protection system; second priority - Low Level RF,  machine protection, power supply control, wire scanner, and OTR profile monitor; and third priority - electro optic bunch length timing, toroid beam charge monitor,  and transverse deflecting cavity bunch length measurement.

These items can best be tested at the FFTB/SPPS beamline early in the project. This area provides access to a short-bunch beam, a FIDO for timing integration, low level RF, and SLC communication. We will need 5 19 inch racks for our equipment as well as room for 3 workstations. In addition, the laser components could be assembled in the laser room in B406 at this site and allow us to complete most of our tests.

The complete list of tests is as follows:

- Test of the Timing System

Is Priority 1 and requires access to PNET and a FIDO.

It will need the following equipment: VME crate, Power PC, PNET receiver in VME*, Event Generator for EPICS timing*, and Event Receiver.

We will demonstrate: proof of integration to the SLC timing, early tests of the event generator, early tests of the event receiver and start development of the timing system events

location: Racks B407A-07 and B407A -08  in Building 406 & 407

When needed: August 2004

What is needed:

| Item | Manufacturer | URL/contact | Dependencies for delivery | Quantity/Price | Total $ |
| --- | --- | --- | --- | --- | --- |
| SLCNet tap (includes MPG) | N/A | Michael Harms, ESD tallmike@slac.stanford.edu | None if done now. Could be done with 1 day’s notice. After summer shutdown, they will be much busier. | 4 hours @ $46 to install RG59 with BNC terminator (cable donated) | 184 92 |
| MDL tap | N/A | Alonzo Baker awb@slac.stanford.edu | Summer shutdown | Quote requested 28jun04 | TBD |
| Linux work station | Dell | SCS | Standard procurement takes 3-6 weeks | 2@$1500 | 3000 |
| VME crate | Wiener Plein & Baus | Andreas Ruben (937) 324-2420 | 8 weeks | 2@$5600 | 11200 |
| PPC IOC | Motorola | unknown | Standard procurement | 2@$4315 | 8630 |
| PNET boards | SLAC subcontractor | Dave Brown, ESD david@slac.stanford.edu | Dave must finish design and send away design for fab | TBD | TBD |
| EVG-110 | Micro-Research Finland Oy | http://www.mrf.fi/evg.html | New version in development. No old available to buy. Maybe can borrow from SLS | 1@0 | 0 |
| EVR-100 | Micro-Research Finland Oy | http://www.mrf.fi/evr.html | As per EVG | 2@0 | 0 |
| R19” rack |  |  | Use existing racks | 2@0 | 0 |
| Ethernet, switch upgrade from 24 to 48 ports | Cisco | Fred Hooker, SCS hooker@slac.stanford.edu | SCS personnel availablity | Switch may be charitable donation from SCS | 0 |
| Terminal Server | Cisco | http://www.cisco.com/en/US/products/hw/routers/ps259/products_data_sheet0900aecd800f414c.html | Standard procurement takes 3-6 weeks | 1 8-port terminal server | 300 |
| TOTAL |  |  |  |  | 23314 |

- Laser Controls

Is Priority 1 and requires access to the laser and access to the timing.

It will require the following equipment: VME crate, Power PC,  Motion Control*, and some Conventional I/O.

We will demonstrate the motion control system, provide an early test stand for conventional I/O, and provide early support for the laser development.

location: Building 261. Using hardware in (1), the following additional hardware is needed:

| Item | Manufacturer | URL/contact | Dependencies for delivery | Quantity/Price | Total $ |
| --- | --- | --- | --- | --- | --- |
| VME58 Intelligent Motion Controller | Oregon Micro Systems | http://www.omsmotion.com/library_files/pdfs/catalog.pdf | Standard procurement | 1@price requested 18jun04 | TBD |
| Digital I/O Module | Xycom | http://www.xycom.com/products/vme/240.html | Standard procurement | 1@price requested 18jun04 | TBD |
| TOTAL |  |  |  |  | TBD |

- Test of the BPMs

Is Priority 1 and requires access to timing and the beamline.

It will require the following equipment: 3 Libera BPM Systems,

We will demonstrate BPM resolution versus bunch charge, prove the BPM integration into the timing and verify that the latency meets fast feedback control requirements.

location: Building 261. Using hardware in (1), the following additional hardware is needed:

| Item | Manufacturer | URL/contact | Dependencies for delivery | Quantity/Price | Total $ |
| --- | --- | --- | --- | --- | --- |
| Libera BPM system | Instrumentation Technologies | Tomaz Karcnik tomaz@i-tech.si | Assume 6 week procurement time | 3@Price requested 18jun2004 | 17700 |
| TOTAL |  |  |  |  | 17700 |

- SLC Aware IOC

Is Priority 1 and requires access to SLC-net over Ethernet and timing

This can be tested in any of the other IOCs.

We will demonstrate integration of EPICS with SLC control system by providing data to SLC with the pulse ID.

location: Building 261. Hardware in (1) is sufficient; nothing additional required

- Bunch length monitor

Is priority 1 and requires access to the beamline and triggers for gated data acquisition.

We will need an insertable CSR monitor and a THz detector with gated ADC data acquisition.

We will demonstrate noninvasive detection of CSR, discriminate between CSR and CTR and CDR effects, single shot correlation with bunch length, and demonstrate the ability to tune to a specific bunch length

location: Building 406 where there is access to beamline. There is access to the timing system at this location, but we could get by with generating our own triggers initially

expected BOE: fall, 2004

| Item | Manufacturer | URL/contact | Dependencies for delivery | Quantity/Price | Total $ |
| --- | --- | --- | --- | --- | --- |
| CSR Monitor | SLAC | Tim Montagne montagne@slac.stanford.edu | In house system design and engineering and external fab | 1 | TBD |
| THz detector | TBR | Patrick Krejcik pkr@slac.stanford.edu | Availability from SPPS | 2 | 0 |
| Gated ADC |  |  |  |  |  |
| Linux workstation | Dell | SCS | Standard procurement takes 3-6 weeks | 2@$1500 | 3000 |
| VME crate | Wiener Plein & Baus | Andreas Ruben (937) 324-2420 | 6 weeks | 1@$5600 | 5600 |
| PPC IOC | Motorola | unknown | Standard procurement | $4315 | 4315 |
| R19” rack | unknown |  |  |  | TBD |
| Ethernet, switch and terminal server | Cisco | Fred Hooker, SCS hooker@slac.stanford.edu | SCS personnel availablity | This could be in place already. Need to ask |  |
| Desks and chairs | N/A | Scrounge from SLAC salvage | availability | N/A | 00 |

- coherent radiation auto correlator

Is priority 1 and requires access to beamline with CSR monitor

We will need a CSR monitor, optical table with mirror control, fine motion control of optical delay, a VME crate, power PC, multi-channel gated data acquisition, and a THz detector.

We will show the absolute measurement of average bunch length profile, verify the THz transport through windows and beam splitters and its effect on measured profile

location: Building 406 where there is access to beamline. There is access to the timing system at this location, but we could get by with generating our own triggers initially

expected BOE: fall, 2004

Using hardware in (5) and assuming we can use existing optical table, the following additional hardware is needed:

| Item | Manufacturer | URL/contact | Dependencies for delivery | Quantity/Price | Total $ |
| --- | --- | --- | --- | --- | --- |
| Fine Motion Optical Delay Controller | Oregon Micro Systems | http://www.omsmotion.com/library_files/pdfs/catalog.pdf | Standard procurement | 1@price requested 18jun04 | ~2700 |
| Motor Power Supply |  |  |  |  | 1000 |
| Motor |  |  |  |  | 3000 |
| TOTAL |  |  |  |  | 6700 |

- Personnel Protection System

Is priority 1 and requires access to the BSY area.

We will need a PLC and an IOC.

We will demonstrate the interface into control system and robust operation in the BSY

location: BSY area

expected BOE: unknown

| Item | Manufacturer | URL/contact | Dependencies for delivery | Quantity/Price | Total $ |
| --- | --- | --- | --- | --- | --- |
| VME crate | Wiener Plein & Baus | Andreas Ruben (937) 324-2420 | 6 weeks | 1@$5600 | 5600 |
| PPC IOC | Motorola | unknown | Standard procurement | 1@$4315 | 4315 |
| 1756 series PLC with s/w, back plane and processor | Rockwell Allen Bradley | http://www.pro-face.com/support/download_e/dw_t/protocol/abcl_df1.htm | Standard procurement | 1@5000 | 5000 |
| TOTAL |  |  |  |  | 14915 |

- Low Level RF

Is priority 2 and requires access to the klystron and timing.

We will need some LLRF control system* along with an interface into the global control system.

We will demonstrate that the LLRF jitter meets our specification, integrates into the timing and that the LLRF latency meets the fast feedback control requirements.

- Machine Protection System

Is priority 2 and requires access to the timing system and  access to the Drive Laser mitigation device

We will need MPS hardware, an Interface from MPS hardware into the control system, VME crate for control system interface, and a Power PC.

We will demonstrate configurable  machine protection with 1 beam pulse shut down time and that the interface to the drive laser mitigation device is operational.

- Power Supply Control

Is priority 2.

We will need an IOC, Power Supply and Power Supply Control.

We will demonstrate appropriate resolution for LCLS magnet control.

- wire scanner monitor

Is priority 2 and requires access to beamline and timing system.

We will need an SLC wire scanner, data acquisition for photomultiplier tube, PM tube HV supply controller, stepping motor controller, position encoder readback

We will demonstrate EPICS data acquisition with timing using a SLC wire scanner, measurement of wire scanner sensitivity versus beam charge and provide testing of new Cherenkov and PM tube configurations

- OTR profile monitor

Is priority 2 and requires access to the beamline and timing.

We will need a profile monitor screen, digital camera and optics, coarse motion actuator and the crate and I/O to control them.

We will demonstrate data acquisition with timing using images from profile monitor, measurements of camera sensitivity versus beam charge, and testing of optical resolution.

- electro optic bunch length timing

Is priority 3 and requires access to beamline with EO monitor and the timing system.

We will need an SPPS EO chamber and optical setup, an SPPS laser pulse, EPICS timing, VME crate, fine motion control optical stage, gated camera image acquisition, and data acquisition synchronous with SCP data.

We will demonstrate measurement of EPICS timing trigger stability w.r.t. e-beam and laser as well as integration of EO data acquisition.

- toroid beam charge monitor

Is priority 3 and requires access to the beamline.

We will need a toroid pickup from Bergoz (already ordered), a VME crate with timing and gated ADC data acquisition.

We will demonstrate EPICS data acquisition with timing using a commercially supplied toroid and measure the toroid accuracy.

- transverse deflecting cavity bunch length measurement

Is priority 3 and requires access to linac and timing

We will need TCAV and a profile monitor.

We will demonstrate data acquisition with timing using image from profile monitor and integration with low level RF for the TCAV. We will provide the application program development for automating bunch length measurement

- LLRF prototyping

Is priority 3 and requires access to …

We will need an RF power meter estimated at $3K and made by Agilent