Signals for "Standard Klystron" Control System

Below is a list of parameters taken from the existing SLC klystron support system and including LCLS requirements.

SLC Fast Time Plots - 10MHz BW  64 data points - 6.5uS

Fast Plots - require

SLED out PHAS & AMPL

Accelerator In PHAS & AMPL		LCLS Required

Accelerator Out PHAS & AMPL 		LCLS Required

Klystron Forward Ampl

Klystron Reflected Ampl

Klystron Drive PHAS & AMPL		LCLS Required

Klystron Reference Phase			LCLS Required

Gold Phase - Calculated

Other Waveforms

Beam Volts					LCLS Required

Beam Current

Perviance - Calculated

Triggers

Modulator Trigger Delay

RF Trigger Delay (The Forgotten One)	LCLS Required

Sub-booster Trigger delay (FETs On)	LCLS Required

Sub-booster RF delay	(DAC start)		LCLS Required

Sample Trigger Delay	(ADC start)		LCLS Required

Analog Signals

Klystron Vacuum

Waveguide Vacuum

Klystron Focus Coil Current

Klystron Heater Power

Thermocouples	12 total

PAD					LCLS Required

MKSU

SSSB					LCLS Required

2X Klystron Windows

3X Accelerator 			LCLS Required

4X Waveguide

Power Supplies

PAD 3X				LCLS Required

SSSB 2X

Control 4X				LCLS Required

References

External Ground			LCLS Required

Differential Ground			LCLS Required

DACs					LCLS Required

ADCs					LCLS Required

Control Signals

DACs I&Q 				LCLS Required

2 Channels

119MHz 8.6uS = 1k Samples / channel

0.03 degrees resolution = 0.5mRadians = 1/2000 = 12 bit DAC

Noise Levels

Assume 12bit peak = 1V input : LSB = 250uV

MUX

* MAX4567 2xSPDT

MAX4564 1xSPDT

14 bit 119MHz DACs

AD AD9775 400MSPS Dual Chan 410mW	Digikey

TI DAC2904 125MSPS Dual Chan 310mW	Digikey

TI DAC5672 200MSPS Dual Chan 330mW

MAX5887 500MSPS Sing Chan 130mW

Summary of LCLS required signals

Channels	Type

4 (8)		FAST ADCs for 50fS phase measurements

3		FAST ADCs for .5pS waveforms

4		Triggers

16		Slow ADCs Thermocouples and Voltages

4		Slow DACs PAD Reference I&Q and offsets
2		Fast DACs Waveform control

LCLS RF Control Signals

Laser - Phase - 120Hz single setting - CW

Gun - Phase and Amplitude - 120Hz Waveform - Pulse shape - 3.5uS 8.4nS

L0A -	Phase and Amplitude - 120Hz single setting plus PSK - 3.5uS 16.8nS

L0B - Phase and Amplitude - 120Hz single setting plus PSK - 3.5uS 16.8nS

L0TCav - Phase and Amplitude - 120Hz single setting - 1uS 16.8nS

L1X - Phase and Amplitude - 120Hz single setting plus pulse - 140nS 8.4nS

L1S - Phase and Amplitude - 120Hz single setting plus PSK - 3.5uS 16.8nS

24-1 - Phase and Amplitude - 120Hz single setting plus PSK - 3.5uS 16.8nS

24-2 - Phase and Amplitude - 120Hz single setting plus PSK - 3.5uS 16.8nS

24-3 - Phase and Amplitude - 120Hz single setting plus PSK - 3.5uS 16.8nS

24-8TCav - Phase - 120Hz single setting - 1uS 16.8nS

S29 - Phase - 120Hz single setting - CW

S30 - Phase - 120Hz single setting - CW

Largest data set  is gun 3.5uS pulse width, 8.4nS steps=417 pts, use 512pts

1kB of data for I and 1kB of data for Q = 2kB at 120Hz in <1mS ~ 20Mbps

X-Band system is 17pts at 119MHz

Laser, S29 and S30 are 4 bytes, set 2 DACs

SLEDed stations, 3.5uS pulse width 16.8nS steps = 256 pts, 1kB at 120Hz

UnSLEDed stations 1uS pulse width 16.8nS steps = 64 pts, 256B at 120Hz

DACs Available

MAX5875 16bit 200MSPS (-162dBFS/Hz@16MHz sig 80MHz -12dBFS)

DAC5687 16bit 500MSPS (-148dBc/Hz@25MHz 6MHz out)

AD9777  16bit 160MSPS (50pA/√Hz)(-100dBFS 5MHz out)

AD9777

1.75W

DAC5687

16MSPS min

750 to 1400mW

MAX5875

260mW

1-200MHz

Klystrons Signals Monitored

Standard Linac Station