Injector and BC1

Magnet Controls

VME, Network and Timing

Signal List

April 6, 2006

Revised: May 22,  2006

Injector:   VME Analog I/O Signals to MCOR Crate #1

| Area | Name | Device Name | MCOR Slot No. | Cable Function | From | To | Cable Function | From | To |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Analog Input | LKG-04-23-S2C-R | LKG-04-07-J4-R | Analog Output | LKG-04-23-S1B | LKG0-07-J3 |
|  |  |  |  | Chan No. | IP-ADC | MCOR Crate | Chan No. | IP-DAC | MCOR Crate |
| GTL | BXG | BTRM:IN20:321 | 1-2 | 0 |  |  | 0 |  |  |
| GTL | QG01 | QUAD:IN20:221 | 3 | 2 |  |  | 2 |  |  |
| GTL | XC01 | XCOR:IN20:221 | 4 | 3 |  |  | 3 |  |  |
| GTL | YC01 | YCOR:IN20:222 | 5 | 4 |  |  | 4 |  |  |
| GUN | CQ01 | QUAD:IN20:121 | 6-7 | 5 |  |  | 5 |  |  |
| GUN | S1BK | SOLN:IN20:111 | 8-9 | 7 |  |  | 7 |  |  |
| GUN | SQ01 | QUAD:IN20:122 | 10-11 | 9 |  |  | 9 |  |  |
| GUN | XC00 | XCOR:IN20:121 | 12 | 11 |  |  | 11 |  |  |
| GUN | YC00 | YCOR:IN20:122 | 13 | 12 |  |  | 12 |  |  |
| LO | QA01 | QUAD:IN20:361 | 14 | 13 |  |  | 13 |  |  |
| LO | QA02 | QUAD:IN20:371 | 15 | 14 |  |  | 14 |  |  |
| LO | XC02 | XCOR:IN20:311 | 16 | 15 |  |  | 15 |  |  |

Injector:  VME Analog I/O Signals to MCOR Crate #2

| Area | Name | Device Name | MCOR Slot No. | Cable function | From | To | Cable function | FROM | To |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Analog Input | LKG-04-23-S3C | LKG-04-15-J4 | Analog Output | LKG-04-23-S2B | LKG0-15-J3 |
|  |  |  |  | Chan No | IP-ADC | MCOR Crate | Chan No. | IP-DAC | MCOR Crate |
| LO | XC03 | XCOR:IN20:341 | 1 | 0 |  |  | 0 |  |  |
| LO | XC04 | XCOR:IN20:381 | 2 | 1 |  |  | 1 |  |  |
| LO | XC05 | XCOR:IN20:411 | 3 | 2 |  |  | 2 |  |  |
| LO | YC02 | YCOR:IN20:312 | 4 | 3 |  |  | 3 |  |  |
| LO | YC03 | YCOR:IN30:342 | 5 | 4 |  |  | 4 |  |  |
| LO | YC04 | YCOR:IN20:382 | 6 | 5 |  |  | 5 |  |  |
| LO | YC05 | YCOR:IN20:412 | 7 | 6 |  |  | 6 |  |  |
| SAB | QS01 | QUAD:IN20:941 | 8 | 7 |  |  | 7 |  |  |
| SAB | QS02 | QUAD:IN20:961 | 9 | 8 |  |  | 8 |  |  |
|  | Spare |  |  | 9 |  |  | 9 |  |  |
| GTL | BXG | BEND:IN20:321 | 11-12 | 10 |  |  | 10 |  |  |
| DL1 | QB | QUAD:IN20:731 | 13-14 | 12 |  |  | 12 |  |  |
| SAB | XCS1 | XCOR:IN20:911 | 15 | 14 |  |  | 14 |  |  |
| SAB | XCS2 | XCOR:IN20:951 | 16 | 15 |  |  | 15 |  |  |

Injector:  VME Analog I/O Signals to MCOR Crate #3

| Area | Name | Device Name | MCOR Slot No. | Cable Function | From | To | Cable Function | From | To |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Analog Input | LKG-04-23-S4C | LKG-03-07-J4 | Analog Output | LKG-04-23-S3B | LKG-03-07-J3 |
|  |  |  |  | Chan No. | IP-ADC | MCOR Crate | Chan No. | IP-DAC | MCOR Crate |
| DL1 | BX01 | BTRM:IN20:661 | 1-2 | 0 |  |  | 0 |  |  |
| DL1 | BXH1 | BTRM:IN20:451 | 3-4 | 2 |  |  | 2 |  |  |
| DL1 | BXH3 | BTRM:IN20:475 | 5-6 | 4 |  |  | 4 |  |  |
| DL1 | BXH4 | BTRM:IN20:481 | 7-8 | 6 |  |  | 6 |  |  |
| DL1 | QE01 | QUAD:IN20:425 | 9 | 8 |  |  | 7 |  |  |
| DL1 | QE02 | QUAD:IN20:441 | 10 | 9 |  |  | 8 |  |  |
| DL1 | QE03 | QUAD:IN20:511 | 11 | 10 |  |  | 10 |  |  |
| DL1 | QE04 | QUAD:IN20:525 | 12 | 11 |  |  | 11 |  |  |
| DL1 | QM01 | QUAD:IN20:631 | 13 | 12 |  |  | 12 |  |  |
| DL1 | QM02 | QUAD:IN20:651 | 14 | 13 |  |  | 13 |  |  |
| DL1 | QM03 | QUAD:IN20:771 | 15 | 14 |  |  | 14 |  |  |
| DL1 | QM04 | QUAD:IN20:781 | 15 | 15 |  |  | 15 |  |  |

Injector:  VME Analog I/O Signals to MCOR Crate #4

| Area | Name | Device Name | MCOR Slot No. | Cable Function | From | To | Cable Function | From | To |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Analog Input | LKG-04-23-S5C | LKG-03-15-J4 | Analog Output | LKG-04-23-S4B | LKG-03-15-J3 |
|  |  |  |  |  | IP-ADC | MCOR Crate |  | IP-DAC | MCOR Crate |
| DL1 | XC06 | XCOR:IN20:491 | 1 | 0 |  |  | 0 |  |  |
| DL1 | XC07 | XCOR:IN20:521 | 2 | 1 |  |  | 1 |  |  |
| DL1 | XC08 | XCOR:IN20:641 | 3 | 2 |  |  | 2 |  |  |
| DL1 | XC09 | XCOR:IN20:721 | 4 | 3 |  |  | 3 |  |  |
| DL1 | XC10 | XCOR:IN20:761 | 5 | 4 |  |  | 4 |  |  |
| DL1 | YC06 | YCOR:IN20:492 | 6 | 5 |  |  | 5 |  |  |
| DL1 | YC07 | YCOR:IN20:522 | 7 | 6 |  |  | 6 |  |  |
| DL1 | YC08 | YCOR:IN20:642 | 8 | 7 |  |  | 7 |  |  |
| DL1 | YC09 | YCOR:IN20:722 | 9 | 8 |  |  | 8 |  |  |
| DL1 | YC10 | YCOR:IN20:762 | 10 | 9 |  |  | 9 |  |  |
| GSPEC | QG02 | QUAD:IN20:811 | 11 | 10 |  |  | 10 |  |  |
| GSPEC | QG03 | QUAD:IN20:831 | 12 | 11 |  |  | 11 |  |  |
| GSPEC | XCG1 | XCOR:IN20:811 | 13 | 12 |  |  | 12 |  |  |
| GSPEC | XCG2 | XCOR:IN20:831 | 14 | 13 |  |  | 13 |  |  |
| GSPEC | YCG1 | YCOR:IN20:812 | 15 | 14 |  |  | 14 |  |  |
| GSPEC | YCG2 | YCOR:IN20:832 | 16 | 15 |  |  | 15 |  |  |

Injector:  VME Analog I/O Signals to MCOR Crate #5

| Area | Name | Device Name | MCOR Slot No. | Cable Function | From | To | Cable Function | From | To |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Analog Input | LKG-04-23-S6C | LKG-03-23-J4 | Analog Output | LKG-04-23-S5B | LKG-03-23-J3 |
|  |  |  |  |  | IP-ADC | MCOR Crate |  | IP-DAC | MCOR Crate |
| SAB | YCS1 | YCOR:IN20:912 | 1 | 0 |  |  | 0 |  |  |
| SAB | YCS2 | YCOR:IN20:952 | 2 | 1 |  |  | 1 |  |  |
|  | Spare |  | 3 | 2 |  |  | 2 |  |  |
|  | Spare |  | 4 | 3 |  |  | 3 |  |  |
|  | Spare |  | 5 | 4 |  |  | 4 |  |  |
|  | Spare |  | 6 | 5 |  |  | 5 |  |  |
|  | Spare |  | 7 | 6 |  |  | 6 |  |  |
|  | Spare |  | 8 | 7 |  |  | 7 |  |  |
|  | Spare |  | 9 | 8 |  |  | 8 |  |  |
|  | Spare |  | 10 | 9 |  |  | 9 |  |  |
|  | Spare |  | 11 | 10 |  |  | 10 |  |  |
|  | Spare |  | 12 | 11 |  |  | 11 |  |  |
|  | Spare |  | 13 | 12 |  |  | 12 |  |  |
|  | Spare |  | 14 | 13 |  |  | 13 |  |  |
|  | Spare |  | 15 | 14 |  |  | 14 |  |  |
|  | Spare |  | 16 | 15 |  |  | 15 |  |  |

LI21:  VME Analog I/O Signals to MCOR Crate #1

| Area | Name | Device Name | MCOR Slot No. | Cable Function | From | To | Cable Function | From | To |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Analog Input | LKG-05-23-S2C | LKG-05-07-J4 | Analog Output | LKG-05-23-S1B | LKG-03-07-J3 |
|  |  |  |  |  | IP-ADC | MCOR Crate |  | IP-DAC | MCOR Crate |
| LI21 | QA11 | QUAD:LI21:131 | 1 | 0 |  |  | 0 |  |  |
| LI21 | QA12 | QUAD:LI21:161 | 2 | 1 |  |  | 1 |  |  |
| LI21 | QM14 | QUAD:LI21:315 | 3 | 2 |  |  | 2 |  |  |
| LI21 | QM15 | QUAD:LI21:335 | 4 | 3 |  |  | 3 |  |  |
| LI21 | XC11 | XCOR:LI21:101 | 5 | 4 |  |  | 4 |  |  |
| LI21 | XC21402 | XCOR:LI21:402 | 6 | 5 |  |  | 5 |  |  |
| LI21 | YC21503 | YCOR:LI21:503 | 7 | 6 |  |  | 6 |  |  |
| LI21 | XCA11 | XCOR:LI21:135 | 8 | 7 |  |  | 7 |  |  |
| LI21 | XCA12 | XCOR:LI21:165 | 9 | 8 |  |  | 8 |  |  |
| LI21 | XCM14 | XCOR:LI21:325 | 10 | 9 |  |  | 9 |  |  |
| LI21 | YC11 | YCOR:LI21:102 | 11 | 10 |  |  | 10 |  |  |
| LI21 | XC21802 | XCOR:LI21:802 | 12 | 11 |  |  | 11 |  |  |
| LI21 | YC21900 | YCOR:LI21:900 | 13 | 12 |  |  | 12 |  |  |
| LI21 | YCA11 | YCOR:LI21:136 | 14 | 13 |  |  | 13 |  |  |
| LI21 | YCA12 | YCOR:LI21:166 | 15 | 14 |  |  | 14 |  |  |
| LI21 | YCM15 | YCOR:LI21:325 | 16 | 15 |  |  | 15 |  |  |

LI21:  VME Analog I/O Signals to MCOR Crate #2

| Area | Name | Device Name | MCOR Slot No. | Cable Function | From | To | Cable Function | From | To |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Analog Input | LKG-05-23-S3C | LKG-05-15-J4 | Analog Output | LKG-05-23-S2B | LKG-03-15-J3 |
|  |  |  |  |  | IP-ADC | MCOR Crate |  | IP-DAC | MCOR Crate |
| BC1 | BX11 | BTRM:LI21:215 | 1-2 | 0 |  |  | 0 |  |  |
| BC1 | BX13 | BTRM:LI21:241 | 3-4 | 2 |  |  | 2 |  |  |
| BC1 | BX14 | BTRM:LI21:261 | 5-6 | 4 |  |  | 4 |  |  |
| BC1 | CQ11 | QUAD:LI21:221 | 7 | 6 |  |  | 6 |  |  |
| BC1 | CQ12 | QUAD:LI21:251 | 8 | 7 |  |  | 7 |  |  |
| BC1 | QM11 | QUAD:LI21:221 | 9 | 8 |  |  | 8 |  |  |
| BC1 | QM12 | QUAD:LI21:271 | 10 | 9 |  |  | 9 |  |  |
| BC1 | QM13 | QUAD:LI21:278 | 11 | 10 |  |  | 10 |  |  |
| LI21 | XCM11 | XCOR:LI21:191 | 12 | 11 |  |  | 11 |  |  |
| BC1 | XCM13 | XCOR:LI21:275 | 13 | 12 |  |  | 12 |  |  |
| BC1 | YCM12 | YCOR:LI21:276 | 14 | 13 |  |  | 13 |  |  |
| LI21 | YCM11 | YCOR:LI21:192 | 15 | 14 |  |  | 14 |  |  |
|  | Spare |  | 16 | 15 |  |  | 15 |  |  |

Injector and LI21:  VME to PLC for MCOR Bulk

| Area | Name | Device Name | Description | I/O Type | Tag No. | Location |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | LKG-03-35 |
| KG |  | LGPS:IN20:3 | PS on/off | DI |  |  |
| KG |  | LGPS:IN20:4 | PS on/off | DI |  |  |
| KG |  | LGPS:IN20:3 | PS on/off | DO |  |  |
| KG |  | LGPS IN20:3 | PS Reset | DO |  |  |
| KG |  | LGPS:IN20:4 | PS on/off | DO |  |  |
| KG |  | LGPS:IN20:4 | PS Reset | DO |  |  |
| KG |  | LGPS:IN20:3 | Set Current | AO |  |  |
| KG |  | LGPS:IN20:4 | Set Current | AO |  |  |
| KG |  | LGPS:IN20:3 | Read Current | AI |  |  |
| KG |  | LGPS:IN20:4 | Read Current | AI |  |  |
| KG |  | LGPS:IN20:3 | Bulk PS 1 Reset | D0 |  |  |
| KG |  | LGPS:IN20:4 | Bulk PS 2 Reset | DO |  |  |
| KG |  | LGPS:LM21:3 | Bulk PS 1 on/off | DI |  |  |
| KG |  | LGPSLM21:3 | Bulk PS on/off | DO |  |  |
| KG |  | LGPS:LM21:3 | Bulk PS Reset | DO |  |  |
| KG |  | LGPS:LM21:3 | Bulk Set Current | AO |  |  |
| KG |  | LGPS:LM21:3 | Bulk Read Current | AI |  |  |

Injector: Digital Input Signals from VME to PPS Aux Box

| Area | Name | Device Name | Cable Function | Cable Type | From | Connector | To | Connector |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| KG | BX01-BX02 | LGPS:IN20:3 | PPS on/off permit | ??? | LKG05-23-S4R-T1 | Screw terminal | LKG05-?? | DB8M |

Injector: Digital Output Signals from VME to PPS Aux Box

| Area | Name | Device Name | Cable Function | Cable Type | From | Connector | To | Connector |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| KG | BX01-BX02 | LGPS:IN20:3 | PPS on/off permit | ??? | LKG05-23-S4R-T? | Screw terminal | LKG05-?? | DB8M |

Timing Signals

| Area | Name | Device Name | Cable Function | Cable Type | From | Connector | To | Connector |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Injector |  | EVR:IN20:KG900 | Event Receiver | Fiber Optic | LKG-04-23-S1-PCI1 |  | LKG-21-27-1 |  |
| BC1 |  | EVR:LI21:KG900 | Event Receiver | Fiber Optic | LKG-05-23-S1-PCI1 |  | LKG-21-27-2 |  |

Network Signals

| Area | Name | Device Name | Cable Function | From | Connector | To | Connector |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Injector |  | IOC_MGNT:IN20:KG900 | CA Ethernet | LKG-04-23-S1-LAN1 | RJ45 | LKG-24-25-1 | RJ45 |
| Injector |  | IOC_MGNT:IN20:KG901 | FFBK Ethernet | LKG-04-23-S1-LAN2 | RJ45 | LKG-24-25-2 | RJ45 |
| Injector |  | IOC_MGNT:IN20:KG902 | VME Crate Mon/Ctrl | LKG-04-23-Ethernet | RJ45 | LKG-24-25-12 | RJ45 |
| Injector | BX01-BX02 | LGPS:IN20:1 | PS Controller | LKG-02-33 | RJ45 | LKG-24-25-3 | RJ45 |
| Injector | BXH1-BXH4 | LGPS:IN20:2 | PS Controller | LKG-02-35 | RJ45 | LKG-24-25-4 | RJ45 |
| Injector | BXS | BEND:IN20:931 | PS Controller | LKG-02-37 | RJ45 | LKG-24-25-5 | RJ45 |
| Injector | S1 | SOLN:IN20:121 | PS Controller | LKG-01-33 | RJ45 | LKG-24-25-6 | RJ45 |
| Injector | S2 | SOLN:IN20:311 | PS Controller | LKG-01-35 | RJ45 | LKG-24-25-7 | RJ45 |
| BC1 |  | IOC_MGNT:LI21:KG900 | CA Ethernet | LKG-05-23-S1-LAN1 | RJ45 | LKG-24-25-8 | RJ45 |
| BC1 |  | IOC_MGNT:LI21:KG901 | FFBK Ethernet | LKG-05-23-S1-LAN2 | RJ45 | LKG-24-25-9 | RJ45 |
| BC1 |  | IOC_MGNT:LI21:KG903 | VME Crate Mon/Ctrl | LKG-05-23-Ethernet | RJ45 | LKG-24-25-11 | RF45 |
| BC1 | BX11-BX14 | LGPS:LI21:2 | PS Controller | LKG-06-33 | RJ45 | LKG-24-25-10 | RJ45 |
| Injector |  |  | IOC Serial Port | LKG-04-23-S1-Bug | RJ45 | LKG-09-48-1 | RJ45 |
| BC1 |  |  | IOC Serial Port | LKG-05-23-S1-Bug | RJ45 | LKG-09-48-2 | RJ45 |
| Injector | BX01-BX02 | LGPS:IN20:1 | EPSC Serial Port | LKG-02-33 | DB25M | LKG-09-48-3 | RJ45 |
| Injector | BXH1-BXH4 | LGPS:IN20:2 | EPSC Serial Port | LKG-02-35 | DB25M | LKG-09-48-4 | RJ45 |
| Injector | BXS | BEND:IN20:931 | EPSC Serial Port | LKG-02-37 | DB25M | LKG-09-48-5 | RJ45 |
| Injector | S1 | SOLN:IN20:121 | EPSC Serial Port | LKG-01-33 | DB25M | LKG-09-48-6 | RJ45 |
| Injector | S2 | SOLN:IN20:311 | EPSC Serial Port | LKG-01-35 | DB25M | LKG-09-48-7 | RJ45 |
| BC1 | BX11-BX14 | LGPS:LI21:2 | EPSC Serial Port | LKG-06-33 | DB25M | LKG-09-48-8 | RJ45 |