# LCLS Magnets

# New Power Supplies

September 30, 2005

The tables below lists the number of new powers supplies for LCLS for the Injector (INJ), BC1, Linac (LI21-LI30), Beam Switch Yard (BSY), Linac to Undulator (LTU) and the Undulator (UND). Carl Rago’s master magnet list and a version of this list massaged by Paul Bellomo for PE needs were used to compile these tables. I also used Paul Bellomo’s presentations for the Injector, BC1 and Linac Power Supply Proposals as a guide in addition to the LCLS Sector 20 Electrical Power Supply Rack Profiles, drawing number ID 381-201-01-C0. I have provided the magnet lists and presentations are listed below.

http:\\www.slac.stanford.edu\grp\lcls\controls\global\subsystems\mgnt\hw\LCLS LCLS Magnets_R7.xls

http://www.slac.stanford.edu/grp/lcls/controls/global/subsystems/magnet/hw/Bellomo_05-11-07_LCLS_Power_Supply_List.xls

http:\\www.slac.stanford.edu\grp\lcls\controls\global\subsystems\mgnt\hw\Injector Intermediate Power Supplies.ppt

http:\www.slac.stanford.edu\grp\lcls\controls\global\subsystems\mgnt\hw\Sector 21 and BC1 Power Supplies.ppt

To interpret the tables below for power supplies connected to an MCOR chassis, note that each MCOR chassis has 16 channels. The distribution of these channels is such that a single MCOR12 power module utilizes one channel where as an MCOR30 power module utilizes two channels. An MCOR12 power module can distribute up to 40V/12A of the bulk, where as an MCOR30 can distribute up to 50V/30A. In addition, an MCOR chassis can be connected to one or two intermediate power supplies connected in parallel. The size of the bulk power supply and number is determined by the power requirements of the magnets.

It is now also important to define a few terms. The first is “Intermediate PS”. An intermediate power supply is a rack mountable powers supply (ie: ≤ 15kW). The second term to define is “Large power supply”, which is any power supply that is larger than 2*15kW or 30kW. A 15kW power supply would be rack mountable whereas a > 30kW supply would be a free standing. The reasons that a 30kW power supply would not be rack mountable is because of weight, size excessive power taken from the rack. In some instances where 30kW is needed to power a magnet or magnet string, two intermediate power supplies of 15kW connected in series or parallel can be used as rack mountable units. The next term is a “Small power supply”, which defines any power supply 2.5kW or less..

A few comments should be made regarding how costs for power supplies can be calculated. An estimate of cost $1 per kW can be used for power supplies, which means that a 60kW power supply would cost approximately 60K or $60,000.00.  The price for small power supplies can be estimated at $1,500 to $2000 each. Kicker power supplies are very special and a rough cost is $50,000. The $50k price tag would include design work be done by the vendor rather than LCLS.  Currently there are two new kickers for LCLS.

The formula to calculate watts is V*A=W. If the required magnet current is known but not the voltage, the following formula can be used to provide a rough estimate of  voltage, V=3/4A. Note: If no magnet specifications are currently available, an estimate of 10kW is used.

In the tables below a magnet strings connected in series is designated in the Name column by

- A list of device names separated by commas. An example of three magnet dipoles connected in series BX11, BX13, BX14

- Two device names separated by two dots.  An example would be of four dipole magnets connected in series would be BXH1..BXH4

In addition, some dipole and quadrupoles have trim coils in addition to an intermediate or large power supply. The trim coils require a small power supply, which typically uses an MCOR. So for example, a dipole magnet string configured in series, with four magnets in the string, and two trim coils may have one intermediate supply and two MCOR channels listed.

### Table 1-1

Table 1-1 provides a list of the new magnet power supplies for the LCLS Injector. Please note that the dipole magnets have trim coils installed which require small power supplies in addition to an intermediate power supply. There are a total of 5 MCOR crates used for the injector. The MCOR channels in table 1-1 below are color coded according to crate.

Note:  * indicates fast feedback

| Area | Type | Name | PS Family | Mcor Chans | Intermediate PS | Large PS | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
| INJ | Bend | BXG BXS BXH1,BXH2, BXH3,BXH4 BX01,BX02 | 60V,165A,10kW 25V,375A,10kW 25V,375A,10kW | 2 2 6 2 | 1 2 1 |  | 60V,165A,10kW 3 trim coils @30A Trim coil @ 30A |
|  | Quad | CQ01 SQ01 QG01 QG02 QG03 QA01 QA02 QE01 QE02 QE03 QE04 QM01 QM02 QM03 QM04 QB QS01 QS02 QS03 |  | 2 2 1 1 1 1 1 1 1 1 1 1 1 1 1 2 1 1 1 |  |  | @ 30A @ 30A Share bulk with correctors and bend trims 30A@4.2V |
|  | Xcor | XC00 XC01 XC02 XC03 XC04 * XC05 XC06 XC07 * XC08 XC09 XC10 XCG1 XCG2 XCS1 XCS2 | 60V,165A,10kW | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 | 1 |  | Share bulk with ycors, quads and bend trims |
|  | Ycor | YC00 YC01 YC02 YC03 YC04 * YC05 YC06 YC07 * YC08 YC09 YC10 YCG1 YCG2 YCS1 YCS2 | 60V,165A,10kW | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 | 1 |  | Share bulk with quad, xcors and bend trims FF @ 10Hz FF @ 10Hz |
|  | Soln | S1BK SOL1 SOL2 | 33V,300A,10kW 33V,300A,10kW | 2 | 1 1 |  | Bucking coil @ 30A |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 66 chans | 8 | 0 |  |

### Table 1-2

Table 1-2 provides a list of the new magnet power supplies for the LCLS Linac sectors 21-31, inclusive. These Linac sectors are referred to as LI21 through LI30. Note that some quadrupole magnets are configured in string series and the power supplies for the string include a bulk power supply in addition to a boost power supply. It is important to note that each quadrupole in the magnet string would not necessarily have an individual boost supply. To find out this type of information.

Please refer to Carl Rago’s master magnet list as well as Paul Bellomo’s presentation on Linac Sector 21 and BC1 Power Supply presentation. Both documents are provided on page one herein. There are a total of 2 MCOR crates used for Linac Sector 21. The MCOR channels are color coded according to crate with BC1 MCOR channels shown in blue.

| Area | Type | Name | PS Family | Mcor Chans | Intermediate PS | Large PS | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
| LI21 | Bend | BX11,BX12, BX13,BX14 | 25V,375A,10kW | 6 | 2 |  | 3 Trim coils @ 30A |
|  | Quad | QA11 QA12 QM14 QM15 CQ11 CQ12 QM11 QM12 QM13 | 60V,165A,10kW | 1 1 1 1 1 1 1 1 1 | 1 |  | Bulk ps |
|  | Xcor | XC11 XC21202 XC21302 XCA11 XCA12 XCM14 XCM11 XCM13 |  | 1 1 1 1 1 1 1 1 |  |  | Share bulk with ycors, quads and bend trims |
|  | Ycor | YC11 YC21203 YC21303 YCA11 YCA12 YCM15 YCM12 YCM11 |  | 1 1 1 1 1 1 1 1 |  |  | Share bulk with xcors, quads and bend trims |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 31 chans | 3 | 0 |  |

| Area | Type | Name | PS Family | Mcor Chans | Intermediate PS | Large PS | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
| LI22 | Bend |  |  |  |  |  |  |
|  | Quad |  |  |  |  |  |  |
|  | Xcor |  |  |  |  |  |  |
|  | Ycor |  |  |  |  |  |  |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  | 0 chans | 0 | 0 |  |
| Total |  |  |  |  |  |  |  |
| LI23 | Bend |  |  |  |  |  |  |
|  | Quad |  |  |  |  |  |  |
|  | Xcor |  |  |  |  |  |  |
|  | Ycor |  |  |  |  |  |  |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 0 chans | 0 | 0 |  |
| LI24 | Bend | BX21,BX22,BX23,BX24 |  | 6 | 2 |  | 3 @30A |
|  | Quad | Q24701A, Q24701B Q24901A, Q24901B Q24601 YC24900 * CQ21 CQ22 QM21 QM22 |  | 1 1 1 | 3 1 1 1 1 1 |  | 2 Power Ten FF @ 10Hz MCOR bulk supply |
|  | Xcor |  |  |  |  |  |  |
|  | Ycor |  |  |  |  |  |  |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 9 chans | 10 | 0 |  |

| Area | Type | Name | PS Family | Mcor Chans | Intermediate PS | Large PS | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
| LI25 | Bend |  |  |  |  |  |  |
|  | Quad |  |  |  |  |  |  |
|  | Xcor | XC25202 * XC25503 * |  | 1 1 | 1 |  | FF @ 10Hz FF @ 10Hz |
|  | Ycor | YC25503 * |  | 1 |  |  | FF @ 10Hz |
|  | Soln |  |  |  |  |  |  |
|  | Kick | BXKIK |  |  |  | 1 | $50k |
| Total |  |  |  | 3 chans | 1 | 1 |  |
| LI26 | Bend |  |  |  |  |  |  |
|  | Quad |  |  |  |  |  |  |
|  | Xcor |  |  |  |  |  |  |
|  | Ycor |  |  |  |  |  |  |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 0 chans | 0 | 0 |  |
| Area | Type | Name | PS Family | Mcor Chans | Intermediate PS | Large PS | Note |
| LI27 | Bend |  |  |  |  |  |  |
|  | Quad |  |  |  |  |  |  |
|  | Xcor |  |  |  |  |  |  |
|  | Ycor |  |  |  |  |  |  |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 0 chans | 0 | 0 |  |
| LI28 | Bend |  |  |  |  |  |  |
|  | Quad |  |  |  |  |  |  |
|  | Xcor |  |  |  |  |  |  |
|  | Ycor |  |  |  |  |  |  |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 0 chans | 0 | 0 |  |
| LI29 | Bend |  |  |  |  |  |  |
|  | Quad |  |  |  |  |  |  |
|  | Xcor |  |  |  |  |  |  |
|  | Ycor |  |  |  |  |  |  |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 0 chans | 0 | 0 |  |
| LI30 | Bend |  |  |  |  |  |  |
|  | Quad |  |  |  |  |  |  |
|  | Xcor |  |  |  |  |  |  |
|  | Ycor |  |  |  |  |  |  |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 0 chans | 0 | 0 |  |

### Table 1-3

Table 1-3 provides a list of the new magnet power supplies for the LCLS Beam Switch Yard Area (BSY) area of the existing machine. Please note that some of the new quad strings have boost power supplies installed as well.

| Area | Type | Name | PS Family | Mcor Chans | Intermediate PS | Large PS | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BSY | Bend |  |  |  |  |  |  |
|  | Quad |  |  |  |  |  |  |
|  | Xcor | XC6 XCA0 |  | 1 1 |  |  |  |
|  | Ycor | YC5 YCA0 | 60V,165A,10kW | 1 1 | 1 |  | Share bulk with xcor |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 4 chan | 1 | 0 |  |

### Table 1-5=4

Table 1-5 provides a list of the new magnet power supplies for the LCLS Linac to Undulator .

| Area | Type | Name | PS Family | Mcor Chans | Intermediate PS | Large PS | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
| LTU | Bend | BY1..BY2 BX31,BX32, BX35,BX36 BYW1,BYW2, BYW3 |  | 1 4 1 | 1 1 2 | 1 | 2 30A trim coils . trim coils share bulk with xcors. |
|  | Quad | QVM1 QVM2 QVB1, QVB2, QVB3 QVM3 QVM4 QDL31..QDL34 QT11,QT13, QT21QT23, QT31,QT33, QT41,QT43 QT12,QT22, QT32,QT42 QEM1 QEM2 QEM3 QEM3V QEM4 QE31..QE36 QUM1 QUM2 QUM3 QUM4 |  |  | 1 1 1 1 1 2 2 2 2 2 2 1 2 1 2 2 2 2 |  |  |
| Area | Type | Name | PS Family | Mcor Chans | Intermediate PS | Large PS | Note |
|  | Xcor | XCVM2 XCVB2 XCVM3 XCDL1 XCQT12 XCDL2 XCQT22 XCDL3 XCQT32 * XCDL4 * XCQT42 XCEM2 XCEM4 XCE31 XCE33 XCE35 XCUM1 XCUM4 | 60V, 165A, 10kW | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 | 1 |  | Share bulk with quads @10V/10A FF @ 120Hz FF @ 120Hz |
|  | Ycor | YCVM1 YCVB1 YCVB3 YCVM4 YCDL1 YCQT12 YCDL2 YCQT22 YCDL3 YCQT32 YCDL4 YCQT42 YCEM1 YCEM3 YCE32 YCE34 YCE36 YCUM2 YCUM3 | 60V, 165A, 10kW | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 | 2 |  | Share bulk with xcors @10V/10A |
|  | Soln |  |  |  |  |  |  |
|  | Kick | BYKIK |  |  |  | 1 | $50K |
| Total |  |  |  | 43 chans | 36 | 1 |  |

### Table 1-5

Table 1-5 provides a list of the new magnet power supplies for the LCLS Undulator .

Please note that the Undulator PS Families listed above only provide a guess as to what might be used. This guess was based on the family of PS that were used in the Injector, BC1 and LI21.  The Note column will list the actual voltage and amperage called for in Carl Rago’s master magnet list.

| Area | Type | Name | PS Family | Mcor Chans | Intermediate PS | Large PS | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Und | Bend |  |  |  |  |  |  |
|  | Quad | QF01 QD01 QF02 QD02 QF03 QD03 QF04 QD04 QF05 QD05 QF06 QD06 QF07 QD07 QF08 QD08 QF09 QD09 QF10 QD10 QF11 QD11 QF12 QD12 QF13 QD13 QF14 QD14 QF15 QD15 QF16 QD16 QF17 | 60V,165A,10kW | 33 | 5 |  |  |

| Area | Type | Name | PS Family | Mcor Chans | Intermediate PS | Large PS | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Xcor | XCUM1 * XCUM2 XCUM3 XCUM4 * XCUM5 XCUM6 XCUM7 XCUM8 XCUM9 XCU1M0 XCUM11 XCUM12 XCUM13 XCUM14 XCUM15 XCUM16 XCUM16 XCUM18 XCUM19 XCUM20 XCUM21 XCUM22 XCUM23 XCUM24 XCUM25 XCUM26 XCUM27 XCUM28 XCUM29 XCUM30 XCUM31 XCUM32 XCUM33 | 60V,165A,10kW | 33 | 1 |  | FF @ .1-.01 Hz FF @ .1-.01 Hz |
|  | Ycor | YCUM1 YCUM2 * YCUM3 * YCUM4 YCUM5 YCUM6 YCUM7 YCUM8 YCUM9 YCUM10 YCUM11 YCUM12 YCUM13 YCUM14 YCUM15 YCUM16 YCUM16 YCUM18 YCUM19 YCUM20 YCUM21 YCUM22 YCUM23 YCUM24 YCUM25 YCUM26 YCUM27 YCUM28 YCUM29 YCUM30 YCUM31 YCUM32 YCUM33 | 60V,165A,10kW | 33 | 1 |  | FF @ .1-.01 Hz FF @ .1-.01 Hz |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 99 chans | 7 | 0 |  |

### Table 1-6

Table 1-6 provides a list of the new magnet power supplies for the LCLS Dump.

| Area | Type | Name | PS Family | Mcor Chans | Intermediate PS | Large PS | Note (*) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Dump | Bend | BYD1..BYD3 | 25V,375A,10kW |  | 1 |  |  |
|  | Quad | QUE1 QUE2 QDMP | 25V,375A,10kW 25V,375A,10kW 25V,375A,10kW |  | 1 1 1 |  |  |
|  | Xcor | XCUE1 XCD3 XCDD | 60V,165A,10kW | 3 | 1 |  |  |
|  | Ycor | YCUE1 YCE3 YCDD |  | 3 |  |  | Share ps with xcors |
|  | Soln |  |  |  |  |  |  |
|  | Kick |  |  |  |  |  |  |
| Total |  |  |  | 6 chans | 5 | 0 |  |