## SLAC Traveler for LCLS Everson-Tesla Quadrupole Magnets

This traveler is intended to cover reception, preparation, mechanical fiducialization, and magnetic measurements of the Everson Tesla quadrupole magnets   Thirty of these magnets were ordered, 12 for the injector, 7 for the linac,  7 for the LTU, and four are spares.

Receiving:

The following information is to be noted upon receipt of the magnets by the SLAC MFD group:

| Received by |  | name |
| --- | --- | --- |
| Date received |  | mm/dd/yy |
| SLAC barcode number: |  | # |
| SLAC drawing number: | SA-380-309-00r0 |  |
| Vendor serial number from magnet label: |  | # |
| SLAC approved electrical safety covers? |  | Y/N |
| SLAC approved lifting eyes? |  | Y/N |
| Shipping Damage? |  | Y/N |
| Vendor tests passed on magnet label? |  | Y/N |

| Place Duplicate BarCode Sticker Here: |  |
| --- | --- |

All paper documentation that accompanies the magnets should be sent to Roger Carr, MS 102

| Paperwork sent: |  | technician name |
| --- | --- | --- |

Preparation:

The following tasks are to be undertaken by the SLAC MFD group to prepare the magnets:

1)  The mirror plates and standoffs are to be removed from these magnets.  Please store these mirror plates and standoffs, and do not discard.

| Mirror plates removed |  | technician name |
| --- | --- | --- |

2)  A beam direction arrow, with text “beam direction”, is to be affixed to the top and connector side of the magnet, preferably by stenciling or rubber stamp, or by sticker supplied by LCLS The arrow is to point away from the face of the magnet that has the coil bus wires.  The coil bus wires are thus on the upstream side of the magnet.   The positive and negative power leads are to be marked with '+' and '-'  stickers, as shown in the wiring diagram.

3)  A 14 gauge multistrand wire with red, non-teflon insulation is to be prepared with spade lugs and installed as shown in the wiring diagram below:

| 14 Gauge Jumper installed |  | installer name |
| --- | --- | --- |

4)  Two 18 gauge multistrand wire jumpers with red, non-teflon insulation are to be prepared with spade lugs and installed as shown in the wiring diagram above.

| 18 Gauge Jumpers installed |  | installer name |
| --- | --- | --- |

5)  The magnet is to be mounted a T-1 stage, oriented according to the correct beam direction, as shown in the photo:

| T-1 Stage Installed |  | installer name |
| --- | --- | --- |

Fiducialization:

Fiducialization may be done before or after magnetic measurements.

The magnet is to be fiducialized by the CMM group.  This will require the installation of removable tooling balls, location of the geometric axis of the pole tips of the magnet, and location of tooling balls with respect to the center of this geometric axis when the poles are aligned precisely at  ±45 degrees to horizontal and vertical axes.

| CMM technician |  | name |
| --- | --- | --- |

URL of on-line CMM fiducialization data:

Magnetic Measurements:

Upon receipt of the magnet, the following information should be recorded:

| Date of arrival to Mag. Meas. group: |  | mm/dd/yy |
| --- | --- | --- |
| Responsible measurement operator name: |  | name |

The magnetic measurements group is requested to perform the following tasks:

1)  Verify that the magnets have mirror plates removed, jumpers correctly installed, and beam direction arrows put on.  Also inspect magnet for any visible flaws and damage.

| Incoming inspection OK |  | technician name |
| --- | --- | --- |

2) Connect the magnet to a bipolar 12-A power supply, preferably an MCOR12.  Use care in turning these supplies on and off to limit current spikes that may occur.  Run the magnet up to 8 A for ~30 minutes to warm it up (record temperature).

| Power supply type |  | text |
| --- | --- | --- |
| Magnet connected and warmed up |  | technician name |
| Magnet temperature achieved |  | deg-F |

3)  Standardize the magnet, starting from 0 to +12 A, then through 3 full cycles from +12 A to 12 A and back up to +12 A, finally ending at 12 A (the MCOR12 ramp rate is not controllable, but a flat-top pause time of 10 seconds is desired at each maximum and minimum current).

| Magnet standardized |  | technician name |
| --- | --- | --- |

4)	Maintaining the history cycle, measure length integrated (Gdl with a calibrated rotating coil, from 12 A to +12 A in 1-A steps, including zero (25 ‘up’ measurements).

| Rotating Coil Designation |  | name |
| --- | --- | --- |
| Rotating coil radius |  | meters |
| Final data file name & run number |  | name and # |

5)	Still maintaining the history cycle, measure (Gdl with a calibrated rotating coil back down from +12 A to 12 A in 1-A steps, including zero (25 ‘down’ measurements).

| Final data file name & run number |  | name and # |
| --- | --- | --- |

6)	Measure field harmonics at 12, 6, +1, +6, and +12 A settings using a 1-inch or 0.8-inch diameter probe.

Coefficients of Magnetic Moment Series (expressed in % of n=2 -> 100%)

| Current (A) | Sextupole % (n = 3) | Dodecapole % (n = 6) | 20-pole % (n = 10) |
| --- | --- | --- | --- |
| 12 |  |  |  |
| 6 |  |  |  |
| +1 |  |  |  |
| +6 |  |  |  |
| +12 |  |  |  |

7)  Measure the inductance and resistance of the full magnet:

| Inductance of full magnet |  | mH |
| --- | --- | --- |
| Resistance of full magnet |  | Ohm |

8)  Record integrated moments:

|  | Integraged Quadrupole Gradient at 12 Amps | Max Integrated Sextupole Error at ± 12 Amps | Max Integrated Dodecaple Error at ± 12 Amps |
| --- | --- | --- | --- |
| specification: | 1.88 T | 1% | 1% |
| measurement: |  |  |  |

| Date of completion of SLAC tests: |  | mm/dd/yyyy |
| --- | --- | --- |

URL of on-line magnetic measurement data:

Upon completion of tests, send traveler to Paul Emma, ms 103

9  Approval and Assignment by Paul Emma:

| Magnet accepted: |  | Y/N |
| --- | --- | --- |
| Assigned Location |  | Mad Deck Name |

Upon completion, send traveler to Kathleen Ratcliffe at mailstop 18

Reference Information:

In a 24 hour measurement of the first article of this magnet type at 10 Amps,  the temperature was found to rise to 31C over an ambient of 20C.   See http://www-group.slac.stanford.edu/met/MagMeas/MAGDATA/LCLS/quad/QM-001/.

In a 36 hour test by Achim Wiedemann at 15.5 Amps, the temperature was found to rise to about 45 C from an ambient of 20C.

The magnet polarity is shown in the schematic diagram below: