LCLS Magnet Application Programming Interface (API)

Listed below are (preliminary) PV names required by HLA clients to control magnets.

Notes:

- One magnet device name – “BEND:IN20:451” is used in the table for clarity.

- Record type is labeled with epics type (to look up its possible fields in epics record reference manul) as well as software type, for quick reference. (Ushort = unsigned 16 bits) Note- only the first few have epics type below – needs to be filled in.

- For a list of all LCLS magnet names and  their associated capabilities, refer to Kristi’s Magnet Database Information spreadsheet:

- http://lcls-dev/tiki-index.php?page=LCLS+Magnet+PS+and+Controls+Subsystem , under Magnet Specifications heading on LCLS Magnet Controls wiki page.

- See discussion that follows the table for PV usage and example scenerios, or proper sequences of operations to be used with the PVs.

| Process Variable (PV) Name | Record Type Epics/SW | Database File Name* | Purpose |
| --- | --- | --- | --- |
| Main Control: |
| BEND:IN20:451:BDES | sub, Float | mgntPhy.db | Set desired B field |
| BEND:IN20:451:FUNC | Mbbo, Ushort | mgntCtrl.db | Function command: 2 = trim 3 = calibrate 4 = standardize 5 = degauss 6 = perturb 7 = zero dac / power supply 8 = reset interlocks 9 = turn on 10= turn off (zeroes dac prior) 11=save bdes 12= load saved bdes 13 =undo bdes |
| BEND:IN20:451:BCTRL | Ao,Float | mgntPhy.db | Set desired B field and auto. perturb (this setpoint does both) |
| BEND:IN20:451:ABORT | Bo,Ushort | mgntCtrl.db | Abort current function |
| BEND:IN20:451:BACTLIMITS.F | Sub, Ushort | mgntPhy.db | Turns off alarm limit calculations (=1); turn on (=0) |
| Readbacks: |
| BEND:IN20:451:BDES.DRVL | Sub,Float | mgntPhy.db | Minimum desired field limit |
| BEND:IN20:451:BDES.DRVH | Sub,Float | mgntPhy.db | Maximum desired field limit |
| BEND:IN20:451:BDES.EGU | String[16] | mgntPhy.db | Engineering unit text |
| BEND:IN20:451:BUSY | Bo,Ushort | mgntCtrl.db | Function State: 0=Ready; 1=Done |
| BEND:IN20:451:BACT | Sub,Float | mgntPhy.db | Actual B field; Valid when corresponding CTRL field=0; or 14 if under feedback control |
| BEND:IN20:451:CTRL.RVAL | Mbbo, Ushort | mgntCtrl.db | Current function being implemented (see FUNC codes above) |
| BEND:IN20:1:CTRLSTATE.RVAL | Mbbo, Ushort | mgntCtrl.db | Function Status/Error Code 0=Done/OK 1= Ramping 2=Waiting 3= Mini-standardizing 4=No Control / Unavailable 5 = Ramp Timeout 6= Error 7 = Timeout 8 = Abort 9 = Disabled 10=Feedback 11= Multi-device func error |
| BEND:IN20:451:BDELTAS.M | Sub,Float | mgntPhy.db | 1=Out of tolerance; 0 In tol. |
| Note: there are more PV names associated with Limits calculations for warning/alarms, if interested.. |
| BEND:IN20:451:BDESSAVE | Ao,Float | mgntTrim.db | Saved bdes |
| BEND:IN20:451:IDES | Ao,float | mgntRaw.db | I calc’ed from BDES |
| BEND:IN20:451:IACT | Float | mgntEPSC.db | Actual PS current |
| BEND:IN20:451:IACTPREVOK | Float | mgntEPSC.db | Previous OK PS current |
| BEND:IN20:451:IRIPL | Float | mgntEPSC.db | Extant ripple current |
| BEND:IN20:451:IMON | Float | mgntEPSC.db | Aux. transductor current |
| BEND:IN20:451:BMON | Float | mgntEPSC.db | Xduct B calc’ed from IMON |
| Feedback Control: |
| BEND:IN20:451:FBCKCTRL | Ushort | mgntFbck.db | Feedback Control: 1=Turn On; 0 = Turn off |
| BEND:IN20:451:BFBCK | Float | mgntPhy.db | Set desired feedback B field and perturb (this does both) |
| Multi-Device: |
| (Control): |
| BEND:IN20:451:SELECT …… | Ushort | mgntCtrl.db | 1=Select this device; 0=unselect this device |
| MGNT:IN20:1:ALLMGNTS | Ushort | mgntList.db | Selects/deselects all devices at once |
| MGNT:IN20:1:FUNC | Ushort | mgntList.db | Perform function on all devices with SELECT=1; Function values same as in BEND:IN20:451:FUNC above |
| (Readback): |
| MGNT:IN20:1:SELECTCNT | Ushort | mgntList.db | Device increments after getting FUNC value that matches MGNT FUNC and INLIST=1. |
| MGNT:IN20:1:DONECNT | Ushort | mgntList.db | Count of how many devices are done with multi-device function. Equals SELECTCNT when MGNT:IN20:1:BUSY=0 |
| MGNT:IN20:1:BUSY | Ushort | mgntList.db | Mulit-device Function State: 0=Ready; 1=Done |
| BEND:IN20:451:INLIST | Ushort | mgntCtrol.db | Set by MGNT SNL after being issued a multi-device “list” function command. Reset by device if function code mismatch |
| MGNT:IN20:1:CTRLSTATE.RVAL | Ushort | mgntList.db | Function Status/Errors same as BEND:IN20:451:CTRLSTATE Plus: 11= Multi-device func error |
| General Configuration (installation): |
| BEND:IN20:451:MADNAME | Float | mgntPhy.db | SLC configured B field |
| BEND:IN20:451:Z | Float | mgntPhy.db | Z of mgnt center (meters) |
| BEND:IN20:451:FBCKAVAIL | Ushort | mgntFbck.db | 1=Feedback avail for device; 0=Unavailable |
| BEND:IN20:451:TRIMDISABLE | Ushort | mgntHsta.db | Trim: 1=Disabled; 0=Enabled |
| BEND:IN20:451:CALBDISABLE | Ushort | mgntHsta.db | Calb: 1=Disabled; 0=Enabled |
| BEND:IN20:451:PTRBDISABLE | Ushort | mgntHstat.db | Ptrb: 1=Disabled; 0=Enabled |
| BEND:IN20:451:ICTRL.DRVL | Float | mgntRaw.db | Min operating current -IMMO[0] |
| BEND:IN20:451:ICTRL.DRVH | Float | mgntRaw.db | Max operating current -IMMO[1] |
| BEND:IN20:451:BDES.DRVL | Float | mgntPhy.db | Min desired field |
| BEND:IN20:451:BDES.DRVH | Float | mgntPhy.db | Max desired field |
| More installation PVs coming to identify PSC hw type, etc |
| (polynomials): |
| BEND:IN20:451:POLYCOEF.A to | Float | mgntPoly.db | First polynomial coefficient, |
| BEND:IN20:451:POLYCOEF.L | Float | mgntPoly.db | (A), thru last (L), (up to 12) |
| (tolerances): |
| BEND:IN20:451:BDELTAS.B | Float | mgntPhy.db | Warning abs tol (TOLS[1]) |
| BEND:IN20:451:BDELTAS.C | Float | mgntPhy.db | Warning fraction (TOLS[2]) |
| BEND:IN20:451:BDELTAS.D | Float | mgntPhy.db | Alarm abs tol (TOLS[3]) |
| BEND:IN20:451:BDELTAS.E | Float | mgntPhy.db | Alarm fraction (TOLS[4]) |
| BEND:IN20:451:BDELTAS.F | Float |  | Monitor tol factor (TOLF) |
| BEND:IN20:451:BDELTAS.M | Float | mgntPhy.db | Trim out of tolerance flag- 1=yes;0=no |
| BEND:IN20:451:IACT.ADEL | Float | mgntRaw.db | Abs tol stdz/calb ATOL[1] |
| BEND:IN20:451:IDELTAS.C | Float | mgntRaw.db | Fractional tol stdz/calb ATOL[2] |
| (boot-time): |
| BEND:IN20:451:BCON | Float | mgntPhy.db | SLC configured B field |
| (occasionally set): |
| BEND:IN20:451:OUTOFSERVICE | Ushort | mgntHsta.db | 1=turned off by op; 0 = on |
| BEND:IN20:451:HSTACTRL | Ushort |  | HSTA setpoint |
| ( for slc compatibility) |  |  | 0x0001 good; 0x002 OK; 0x0008 sick; 0x0010 off; 0x0040 feedback control; 0x0080 mini-stdz req’ed; 0x0100 no calibration; 0x0200 no perturb; 0x0400 no trim; 0x0800 no standardize; 0x1000 no retry for trim; 0x2000 stdz down direction; |
| Status: |
| BEND:IN20:451:STATUS | Float |  | Worst case overall status of device - TBD |
| BEND:IN20:451:UNAVAILABLE | Float | mgntStat.db | Power Supply OFF OR Under Feedback Control OR Out of Service |
| BEND:IN20:451:HSTA ( for slc compatibility) | Ushort |  | HSTA readback; see above codes for HSTACTRL |
| BEND:IN20:451:STAT ( for slc compatibility) | Ushort |  | 0x0001 good; 0x0002 OK; 0x0004 dead; 0x0008 sick; 0x0010 off; 0x0020 stdz ok; 0x0040 calb ok; 0x0080 drifting; 0x0100 db error; 0x0200 dac error; 0x0400 adc error; 0x0800 bad current; 0x1000 out of tolerance; 0x2000 bad ripple; 0x4000 bad bact |
| More status coming (ie faults by device type, ..) |
| Standardization: |
| (Configuration): |
| BEND:IN20:451:STDZDISABLE | Ushort | mgntHsta.db | Stdz: 1=Disabled; 0=Enabled |
| BEND:IN20:451:STDZMINI | Ushort | mgntHsta.db | Mini-stdz: 1=Enabled; 0=Dis’ |
| BEND:IN20:451:STDZCYCLENUM | Ulong | mgntStdz.db | Num. cycles (up/down = 1) (NSCY[1]) |
| BEND:IN20:451:STDZSETL | Ulong | mgntStdz.db | Stdz Settling time (NSCY[2]) |
| BEND:IN20:451:STDZIMIN | Float | mgntStdz.db | Stdz min. current (IMMS[1]) |
| BEND:IN20:451:STDZIMAX | Float | mgntStdz.db | Stdz max. current (IMMS[2]) |
| BEND:IN20:451:STDZIFINAL | Float | mgntStdz.db | Stdz final current (IMMS[3]) |
| BEND:IN20:451:STDZDIRECT | Ushort | mgntStdz.db | Stdz direction; 0=Up;1=Down |
| BEND:IN20:451:STDZRAMPRATE | Float | mgntStdz.db | Stdz ramp rate amps/sec |
| (Control): |
| BEND:IN20:451:CTRL=4 |  |  | Initiate standardization |
| (Readback): |
| BEND:IN20:451:STDZOK | Ushort | mgntStdz.db | Stdz’ed: 1=Yes; 0=No |
| BEND:IN20:451:STDZCYCLECNT | Ulong | mgntStdz.db | Half cycles completed |
| BEND:IN20:451:STDZTOD | timestamp | mgntStdz.db | Last time stdz successful |
| BEND:IN20:451:STDZLOSTTOD | timestamp | mgntStdz.db | Last time stdz was lost |
| BEND:IN20:451:IDELTAS | Float | mgntRaw.db | Calc’ed tolerance used stdz. |
| Trim: |
| (Configuration): |
| BEND:IN20:451:TRIMTYPE | Ushort | mgntTrim.db | Trim type: 0=three-linear (default); 1=Linear |
| BEND:IN20:451:TRIMMAXNUM | Ushort | mgntTrim.db | Max Trim Tries (default 10) |
| BEND:IN20:451:TRIMSETTLE | Ulong | mgntTrim.db | Trim Settling time () |
| BEND:IN20:451:TRIMTRYCNT | Ulong | mgntTrim.db | # trim tries (at least 3 for trim type of three-linear) |
| BEND:IN20:451:TRIMTOD | timestamp | mgntTrim.db | Last trim time (KTIM) |
| (Control): |
| BEND:IN20:451:CTRL=2 |  |  | Initiate trim |
| (Readback): |
| BEND:IN20:451:BDESPREVTRIM | Float | mgntPhy.db | BDES from last trim (used for undo function) |
| Calibration: |
| (Configuration): |
| BEND:IN20:451:CALBIMIN | Float | mgntCalb.db | Calb min current (IMMS[1]) |
| BEND:IN20:451:CALBIMAX | Float | mgntCalb.db | Calb max current (IMMS[2]) |
| (Control): |  |  |  |
| BEND:IN20:451:CTRL=3 |  |  | Initiate calibration |
| (Readback): |
| BEND:IN20:451:CALBOK | Ushort | mgntCalb.db | 1=Calb is good; 0=not good |
| BEND:IN20:451:CALBGOODFIT | Float | mgntCalb.db | Calb good fit |
| BEND:IN20:451:CALBTOD | timestamp | mgntCalb.db | Calb time of day |
| BEND:IN20:451:CALBOFFSET | Float | mgntCalb.db | Calc’ed (theoretical)offset |
| BEND:IN20:451:CALBSLOPE | Float | mgntCalb.db | Calc’ed slope (I-DAC conv) |
| BEND:IN20:451:OFFSET | Float | mgntCalb.db | Measured offset during calb |
| BEND:IN20:451:SLOPE | Float | mgntCalb.db | Measured slope during calb |
| Power Supply – Ethernet PSC: |
| Note: later we may have PVs under headings All PSCs, EPSC only, MCOR only, Soft only …TBD |
| Control: |
| BEND:IN20:451:ICTRL | Float | mgntRaw.db | Set PS current |
| BEND:IN20:451:OUTOFSERVICE | Ushort | mgntHsta.db | 1=Out of service; 0 = In-service |
| BEND:IN20:451:IRAMPRATE | Float | mgntRaw.db | Ramp Rate (amps/sec) |
| Readback: |
| BEND:IN20:451:STATE | Ushort | mgntEPSC.db | 1=PS On; 0 = PS OFF |
| BEND:IN20:451:READY | Ushort | mgntEPSC.db | 1=Ready; 0=Not ready |
| BEND:IN20:451:MODE | Ushort | mgntEPSC.db | 1=Remote; 0 = Local |
| BEND:IN20:451:IRIPLOK | Float | mgntEPSC.db | ripple current OK |
| BEND:IN20:451:MGNT0STATUS | Ushort | mgntEPSC.db | I/L 0 status:1=OK; 0=Fault |
| BEND:IN20:451:MGNT1STATUS | Ushort | mgntEPSC.db | I/L 1 status:1=OK; 0=Fault |
| BEND:IN20:451:MGNT2STATUS | Ushort | mgntEPSC.db | I/L 2 status:1=OK; 0=Fault |
| BEND:IN20:451:MGNT3STATUS | Ushort | mgntEPSC.db | I/L 3 status:1=OK; 0=Fault |
| BEND:IN20:451:IACTSTATUS | Ushort | mgntEPSC.db | Xduct1 I/L: 1=OK; 0=Fault |
| BEND:IN20:451:IMONSTATUS | Ushort | mgntEPSC.db | Xduct2 I/L: 1=OK; 0=Fault |
| BEND:IN20:451:IGNDSTATUS | Ushort | mgntEPSC.db | Gnd Curr: 1=OK; 0=Fault |
| BEND:IN20:451:FAULTSTATUS | Ushort | mgntEPSC.db | Fault Latch: 1=OK; 0=Fault |
| BEND:IN20:451:PS0STATUS | Ushort | mgntEPSC.db | PS 0: 1=OK; 0=Fault |
| BEND:IN20:451:PS1STATUS | Ushort | mgntEPSC.db | PS 1: 1=OK; 0=Fault |
| BEND:IN20:451:PS2STATUS | Ushort | mgntEPSC.db | PS 2: 1=OK; 0=Fault |
| BEND:IN20:451:PS3STATUS | Ushort | mgntEPSC.db | PS 3: 1=OK; 0=Fault |
| BEND:IN20:451:CALBSTATUS | Ushort | mgntEPSC.db | PS 3: 1=OK; 0=Fault |
| BEND:IN20:451:HWSTATUS | Ushort | mgntEPSC.db | HW: 1=OK; 0=Fault |
| BEND:IN20:451:INFOMSG | string | mgntEPSC.db | Last text message |
| BEND:IN20:451:IACTINP | Float | mgntEPSC.db | Xduct. 1 current |
| BEND:IN20:451:IDAC | Float | mgntEPSC.db | DAC current |
| BEND:IN20:451:IGND | Float | mgntEPSC.db | Ground current |
| BEND:IN20:451:PSVOLT | Float | mgntEPSC.db | Output voltage |
| BEND:IN20:451:CONTROLTEMP | Float | mgntEPSC.db | Control Temperature |
| BEND:IN20:451:SPAREVOLT | Float | mgntEPSC.db | Spare voltage |
| BEND:IN20:451:ADCOFFSET | Float | mgntEPSC.db | ADC Offset (%) |
| BEND:IN20:451:ADCGAIN | Float | mgntEPSC.db | ADC Gain (%) |
| BEND:IN20:451:DACOFFSET | Float | mgntEPSC.db | DAC Offset (%) ; same as CALBOFFSET |
| BEND:IN20:451:DACGAIN | Float | mgntEPSC.db | DAC Gain (%); same as CALBSLOPE |
| BEND:IN20:451:RESETCODE | Long | mgntEPSC.db | Last reset code |
| BEND:IN20:451:STATEOFFCODE | Long | mgntEPSC.db | Last turn-off code |
| BEND:IN20:451:SELFTESTCODE | Long | mgntEPSC.db | Self-test error code |
| BEND:IN20:451:CALBCODE | Long | mgntEPSC.db | Calb error code |
| BEND:IN20:451:IPADDRESS | String | mgntEPSC.db | IP Address |
| BEND:IN20:451:CHASSIS | Long | mgntEPSC.db | Chassis type |
| BEND:IN20:451:SERIALNUMBER | String | mgntEPSC.db | Serial Number |
| BEND:IN20:451:MAGNETID | String | mgntEPSC.db | Magnet ID |
| BEND:IN20:451:FWVERSION | String | mgntEPSC.db | FW Version number |
| BEND:IN20:451:COMMANDCNT | Long | mgntEPSC.db | Ethernet command count |
| BEND:IN20:451:IACTV2I | Float | mgntEPSC.db | Xduct 1 V/I constant |
| BEND:IN20:451:IMONV2I | Float | mgntEPSC.db | Xduct 2 V/I constant |
| BEND:IN20:451:IGNDV2I | Float | mgntEPSC.db | Gnd current V/I constant |
| BEND:IN20:451:PSVOLTV2V | Float | mgntEPSC.db | PS V/V constant |
| BEND:IN20:451:PSVOLTREF | Float | mgntEPSC.db | PS referenct voltage |
| NOTE: any analog PV postfixed with: |  |  |  |
| .EGU | String[16] |  | Engineering units |
| .DRVH | Float |  | High limit |
| .DRVL | Float |  | Low limit |
| .PREC | Float |  | Precision |

* Full path for database file name = /afs/slac/g/lcls/epics/site/src/micro/epicsmgnt/Db

Discussion

- Note (again): For a list of all LCLS magnet names and  their associated capabilities, refer to Kristi’s Magnet Database Information spreadsheet:

http://lcls-dev/tiki-index.php?page=LCLS+Magnet+PS+and+Controls+Subsystem , under Magnet Specifications heading on LCLS Magnet Controls wiki page.

- To set BDES desired field:

Set  BEND:IN20:451:BDES = <desired field>,  within low limit =

BEND:IN20:451:BCTRL.DRVL , and high limit = BEND:IN20:451:BCTRL.DRVH.

This setpoint must be followed up with a function command – see values described in table above for BEND:IN20:451:FUNC.  Engineering unit can be read in BEND:IN20:451:EGU.

- To Perturb :

Set BEND:IN20:451:BCTRL to within limits BEND:IN20:451:BCTRL.DRVL to .DRVH. This one command sets BDES desired field and perturbs as well.

(Alternate: set BEND:IN20:451:BDES first, then set BEND:IN20:451:CTRL = 6)

- To perform any magnet Function:

  - To Trim:                BEND:IN20:451:FUNC = 2 (also see Trim Scenerio below)

  - To Calibrate:       BEND:IN20:451:FUNC = 3

  - To Standardize:   BEND:IN20:451:FUNC = 4

  - To Degauss:        BEND:IN20:451:FUNC = 5 (one quad only to start)

  - To Perturb:          see “To Perturb” bullet above

  - To Zero PS:         BEND:IN20:451:FUNC = 7 (zeroes dac prior to turn off)

  - To Reset PS interlocks: BEND:IN20:451:FUNC = 8

  - To Turn On PS:   BEND:IN20:451:FUNC = 9

  - To Turn Off PS:  BEND:IN20:451:FUNC = 10

- To check when any (perturb, trim, stdz, etc) Function has completed:

Done when BEND:IN20:451:BUSY = 0; busy when BEND:IN20:451:BUSY = 1.

This can be implemented as a monitor on BEND:IN20:451:BUSY.

- To read BACT actual field:

Read BEND:IN20:451:BACT for actual field. (More stable after any function when BEND:IN20:451:BUSY=0.)

- To check state before using device:

Read BEND:IN20:451:BUSY to make sure =0 – not busy.

Optional: Read BEND:IN20:451:UNAVAILABLE to make sure = 0 – available.

BEND:IN20:451:UNAVAILABLE = 1 when PS off or out of service, or feedback control is ON.

Note:  Transparent to this API, if a function is issued that can’t be done, such as a trim on a device that has trim disabled (BEND:IN20:451:TRIMDISABLE=1), or if  calibration is required (BEND:IN20:451:CALBDISABLE=0) and device hasn’t been calibrated (BEND:IN20:451:CALBOK=0), or if the device is unavailable

(BEND:IN20:451:UNAVAILABLE =1) , an error is issued in BEND:IN20:451:CTRLSTATE.RVAL after the function is set via BEND:IN20:451:FUNC. Thus, depending on functionality, the user doesn’t  have to check status, other than BUSY, prior to issuing a command. The user should always check BEND:IN20:451:CTRLSTATE.RVAL after issuing a command to see if it was successful.

- To check status after function completes:

Read BEND:IN20:451:CTRLSTATE.RVAL when BEND:IN20:451:BUSY=0 (not busy) for relevant status codes:

  - 0=  Done/OK (Successful)

  - 6=  Error

  - 7 = Timeout

  - 8 = Abort

  - 9 = Disabled

  - In addition -Read BEND:IN20:451:BACTLIMITS.F to see if  BDES/BACT is out of tolerance, if relevant to the function (ie for trim, perturb)

- Example Trim Sequence of events :

Read BEND:IN20:451:BUSY to see if =0, NOT busy

Set BEND:IN20:451:BDES to within limits BEND:IN20:451:BCTRL.DRVL to

.DRVH.

Set BEND:IN20:451:CTRL = 2. (will cause BEND:IN20:451:BUSY to set, =1)

Monitor BEND:IN20:451:BUSY for value = 0.

Read BEND:IN20:451:CTRLSTATE.RVAL; =0 if trim was successful; = non-zero if error occurred.

Optional:

Read BEND:IN20:451:BACT for actual field; BEND:IN20:451:BMON etc

Read BEND:IN20:451:BACTLIMITS.F to see if the trim is out of tolerance.

Read BEND:IN20:451:?? TBD for power supply interlock status…

Etc.

- To turn on Feedback Control (when BEND:IN20:451:FBCKAVAIL=1):

Set desired feedback field BEND:IN20:451:BFBCK to within the limits of  BEND:IN20:451:BCTRL.DRVL and .DRVH.  This one command will perturb as well as set desired field. Set BEND:IN20:451:BFBCKCTRL=1 to turn feedback on, if not already on. Done when BEND:IN20:451:BUSY = 0.  (This can be implemented as a monitor on BUSY)

- To perform one Function on a group of magnets at once (per ioc) – use multi-select control:

If  MGNT:IN20:451:BUSY =0, multi-select function is available for use.

Deselect all magnets in ioc first by setting MGNT:IN20:451:ALLMGNTS = 0.

Repeat: if  BEND:IN20:451:BUSY =0,  magnet may be selected by setting its BEND:IN20:451:SELECT =1.  MGNT:IN20:1:SELECTCNT contains number of selected magnets in the ioc.

Perform desired group function by setting MGNT:IN20:1:FUNC=value.

All units are complete when master MGNT:IN20:1:BUSY=0.

MGNT:IN20:1:CTRLSTATE.RVAL contains worst severity status/error codes from all devices included.

What else would you like more detail on?