Event Diagnosis using Correlation

Adnan Iqbal, Yee T. Lee, Les Cottrell

{adnan,ytl,Cottrell} @ slac.stanford.edu

Abstract

Large scale computer networks suffer from performance drops very frequently. Tools and techniques exist to measure these drops in performance. Finding the actual cause of such events is an important requirement to mitigate such problems quickly; however cause detection for such events is a non trivial task and researchers are not very successful to accomplish it. In this paper we have presented novel approaches to figure out the actual cause(s) of a problem. We have also presented results achieved after applying these schemes. All experiments mentioned in this paper have been performed on IEPM [4] [7] network.

1. Introduction

Network performance monitoring is an important part of network management. It helps to provide an estimate of existing network conditions. It includes many activities such as identifying drops in network performance. These performance drops (events) can be caused by a number of reasons including route changes, end host problems or misconfigurations.

Finding such performance drops and diagnosing them is not a trivial task. Our ultimate goal is to pin point the actual cause(s) of such an event. To achieve this purpose a number of steps have to be performed. First requirement is the availability of a large scale monitoring network providing access to relevant results. We have a large monitoring network in the form of the IEPM network. This network consists of monitoring nodes and monitored nodes spread over continents. Different measurement tools have been deployed on the  IEPM network including pathchirp[1], pathload[3], iperf[2] etc. These tools provide network performance measurements periodically. Traceroutes between each pair of monitoring and monitored node are also obtained periodically.

A second layer built upon this measurement infrastructure is that of event detection. It is impossible to analyze all data manually by eye to see the trend and to figure out performance drops. After a careful study of different algorithms to automate the detection of performance changes the  plateau [4] algorithm has been deployed on the IEPM network. As a result of this deployment, we are notified of each significant network performance drop as an e-mail in near to real time. We also have graphical display of such events so that further analysis is easy to be performed.

These two basic steps are necessary but not enough. A third layer of tools is required to be able to diagnose an event detected as network performance drop. This paper is the description of our efforts to solve this problem. We have identified different approaches to solve the problem. Section 2 describes such approaches. Section 3 describes an example case study. Section 4 describes results and section 5 describes conclusion and future directions for this work.

2. Approaches used

We have identified two different approaches to solve this problem; statistical and heuristics based. Both approaches are based on a similar basic concept i.e., to discover correlation between different events occurring at the same time. Principal Component Analysis (PCA) has proved to be a reasonable choice for network anomaly detection [5] [6]. We have extended the PCA approach to figure out correlations between network events so that cause of event can be explored. The other approach is based on heuristics. We have shown that a pure mathematical or statistical approach may not be successful as it is very difficult to model large scale networks. It is also important to constantly improve the scheme as new rules are discovered which may not be possible in a pure mathematical technique. The following two sub sections describe these two schemes in detail.

2.1 Principal Component Analysis

PCA is a well known statistical technique used in many applications. Its basic functionality is dimensionality reduction. Dimensionality reduction is achieved by representing data in terms of principal axes. Once data has been categorized as more common and thus described by the more important principal axes. The higher order principal axes then are likely to contain information related to abnormal events. The following paragraph describes the methodology used for this purpose.

The PCA input data should be multiple time series that provide different views of overlapping network paths. The differences may be in terms of the metric being measured, or the direction in which the path or sub-path is measured.. We have applied this scheme to a data set ranging from three parameters to eight different parameters. Original data may have anomalous readings. Such anomalous readings are discarded using a trimming procedure   so that the analysis is not biased by erroneous values of data. Data is collected from IEPM which provides real measurements from a real high-performance production network. Thus it is always possible to have missing readings because of end-system or network outages. To overcome this problem data regularization is performed. Our regularization algorithm is very simple. Data is regularized in bins of 10 minutes. All values between t1 to t2 such that t2-t1=10 minutes are averaged. If there is no entry in any given period, average of all such periods in on same day of week is calculated. Next data from different related links is combined.

After these preliminary steps, PCA is applied. Principal components are calculated and arranged in order of significance. We calculate abnormal space using most principal component. Event detection is applied to find out anomalies in this data set. All anomalies found in this case are analyzed and recorded. This process is repeated using different variants so that analysis is comprehensive.

2.2 Heuristics based approach

Defining networks and coming up with a consistent and comprehensive model for network diagnostics may not be a suitable idea. Given the problems encountered with PCA we decided to explore a more heuristic approach. Our initial studies strengthened encouraged us to carry on further research in this field.

We came up with two different levels of rules; basic level and low level. Basic level rules help us give general idea that where does the problem lie. Low level heuristics are than used to actually pin point exact problem.

2.2.1 Basic rules

- If an event E is detected at time T, from   a monitoring host H for a monitored node M and there exist other events reported by the same monitoring host H for monitored nodes other than M, then the probability that the monitoring host is causing problem increases with every such result.

Where i represents only those nodes which reported an event and α represents the score each such incident

- If an event E is detected at time T, from a monitoring host H for a monitored node M and there exist other events reported by different monitoring hosts for the                                                                                                                                                                                                                                                                                                                                       same monitored node, then the probability that the monitoring host is causing the problem increases with every such result.

Where i represents only those hosts which reported anevent and β represents the score each such incident

- If an event E is detected at time T, from a monitoring host H for a monitored node M and there exist other events reported by M for H in a similar time period then it confirms that event is not a false alarm. However, its cause can be any of the route change, network problem and or any of the end host.

Where Sx represents score for each category x.

- If an event E is detected at time T, from a monitoring host H for a monitored node M and there exist a change in the number of hops at the time of event detection then there is an increased possibility that the performance drop is caused by a network problem.

Where Snetwork represents the score for a network problem.

Now we have scores for node being monitored (γ), monitoring node (μ) and network problem (λ).

2.2.2 Low level rules

Basic rules give us hints about the actual cause of network performance drop. To reach final conclusion more analysis is required. This analysis is of different types. If we find that an event is probably due to end host problems and we know which end host may be the culprit then we need to analyze all relevant available data for that end host. This data includes performance stats from different devices like CPU, memory and I/O devices.

If an event appears to occur because of any network problem than we need to analyze metrics related to network variations. Network problems can be of many types such as router failure, link failure, congestion and mis-configured devices. Trace routes is valuable information that can be analyzed in different ways to reach the conclusion. One such scenario is when we noticed a route change and figured out that problem is some where in the network. To investigate further we use trace routes with following rules.

If route at t1 is different from t2 and bandwidth recorded for new route is significantly less than that of previous one than it shows that performance drop is due to problem in router or link. Now to find out whether it is a link failure or device failure, we need router statistics for every router along the path for a period significantly greater than t1+t2 and inclusive of both t1 and t2. Analysis of such data will reveal when any device along the path stopped responding. Work is under process to make such data available using PerfSONAR[9].

3. Case Study

In Dec 05, a network performance drop was reported from Brook Haven National Laboratory (BNL) to Node1.ac.uk. After analysis we found following results. We had no reverse path information as node1.dl.ac is not a monitoring node. No other event was reported for node1.dl.ac.uk in similar time frame from any other monitoring node. Numbers of events were reported from BNL to different other monitored nodes. This analysis showed that most probably problem lies with in administrative domain of BNL. All this process was performed manually. It took several days to reach this conclusion because we were not able to see all related events at one time. We had to correlate all related events manually. Related trace routes were collected and analyzed by eye ball. This case study forced us to have an automated system for all this process.

After developing the heuristics based system’s prototype, when similar problem was analyzed using the prototype, same results were obtained in very small time frame. Reaching conclusion was matter of few hours after the detection of performance drop. Even this delay can be minimized by fine tuning the system. Details of this case study can be seen at [8].

4. Results

We have applied PCA to find correlation between different event for different routes and tools. Here we are presenting results obtained from following pairs of nodes; SLAC-DESY, SLAC-SWITCH, SLAC-CESNET, SLAC-FZK, SLAC-NIIT, SLAC-TRIUMF. Results are described in Table 1. We find some correlation in case of Desy, Fzk and NIIT but these results do not guide us towards any particular important outcome in general.

We have deployed event diagnostics using heuristics at SLAC and results are also available online at [10]. All events detected since start of 2005 to date are analyzed and every newly discovered performance drop is analyzed automatically and result summary is sent to concerned via e-mail. Here we describe analysis result for problem mentioned in case study. When Analyzed using event diagnostics system, every alert reported produced a non zero score for monitoring host issues and zero for other categories i.e., route change, reverse path analysis and end host, which tells us that problem lies within monitoring node domain. This showed that results obtained through manual analysis and automated systems are same. Trace routes are also analyzed and autonomous system’s appearance frequency is also calculated. For complete analysis output, look at [11]. There are other interesting cases such as [12][13].

|  | Cesnet | Desy | Fzk | NIIT | Switch | Triumf |
| --- | --- | --- | --- | --- | --- | --- |
| (1)Events detected in multi-route#1 | 20 | 20 | 20 | 20 | 20 | 20 |
| (2)Events detected in multi-rout#1 excluding node in title | 20 | 20 | 23 | 17 | 20 | 20 |
| Overlapping events in 1 and 2 | 20 | 3 | 7 | 10 | 20 | 20 |
| single route events overlapping with Events detected in 1 | 3 | 6 | 8 | 6 | 1 | 1 |
| single route events overlapping with Events detected in 1 and 2 | 3 | 3 | 5 | 1 | 1 | 1 |

Table 1. Finding Correlation using PCA

| Event | Route Change | Host | Target | Network |
| --- | --- | --- | --- | --- |
| BNL Dec 05 | 0 | 100 | 0 | 0 |
| Taiwan Dec 06 | 0 | 400 | 0 | 0 |
| SLAC Nov 06 | 0 | 50 | 200 | 0 |

Table 2. Results from heuristics, BNL Dec 05 [11], Taiwan July 05[12], SLAC Nov 06[13]

| Events detected & analyzed | 1379 |
| --- | --- |
| Events resulting in any non zero score | 811 |
| Event correlated with other events | 772 (56% of total) |
| Stand alone events (no correlation) | 607 |

Table 3. Total alerts analyzed and their correlation output (March 2005 - Dec 2006)

5. Conclusion & Future Directions

We have shown in this paper that correlation based approaches can help to figure out actual cause of network performance drop and help network administrators to pinpoint exact location of network problem. It has also been confirmed that heuristics based approach is more useful than Principal Component Analysis. Heuristics based approach also has potential to be upgraded when new rules are discovered. Our proposed future work is to extend this scheme such that it involves detailed analysis of network problems as well as end host analysis. Another direction for future work is to integrate all this work with PerfSonar [9]. We are also working to standardize network measurement parameters so that network diagnostic tools can also be standardized.

6. References

1. Vinay J. Ribeiro,Rudolf H. Riedi,Richard G. Baraniuk, Jiri Navratil, Les Cottrell, “pathChirp: Efficient Available Bandwidth

Estimation for Network Paths”, PAM2003

2. http://dast.nlanr.net/Projects/Iperf/

3. Manish Jain, Constantinos Dovrolis, “ Pathload: A measurement tool for end to end available bandwidth“, PAM2002

4. Connie Logg, Les Cottrell, Jiri Navratil, “Experiences in Traceroute and Available Bandwidth Change Analysis”, sigcomm2004

5. Anukool Lakhina, Mark Crovella and Christophe Diot. “Diagnosing Network-Wide Traffic Anomalies,” In Proceedings of ACM SIGCOMM 2004

6. ADAM: A Practical Approach for Detecting Network Anomalies Using PCA, “Arshad Ali, Modood Ahmad Khan, S. Azam H. Bukhari and Waqar Mahmood”, NCET2004

7. https://confluence.slac.stanford.edu/displa y/IEPM/Home

8. http://www.slac.stanford.edu /grp/scs/net

/ca se/bnl_dec05/

9. perfSonar

http://www.perfsonar.net/

10. http://www-iepm.slac.stanford.edu /monitoring/event-diagnosis/analysis/sum mary .html

11. http://www-iepm.slac.stanford.edu /monitoring/event-diagnosis/analysis/iepm-bw.bnl.org-node1.pd.infn.it-1135819560.html

12. http://www-iepm.slac.stanford.edu/ monitoring/event-diagnosis/analysis/iepm-bw.twaren.net-node1.indiana.edu-1165323071.html

13. http://www-iepm.slac.stanford.edu /monitoring/event-diagnosis/analysis/iepm-bw.slac.stanford.edu-node1.cacr.caltech.edu-1163213922.html

# Comments

Not sure what to call it, not sure network is the right thing

Which two basic steps? The automated detection and the alerting via email, or the automated detection and the provision of graphical displays to assist the human in interpretring/validatingt the event?

I am not sure what you mean here, do you mean: the average of  all such periods in the same day of the week for the last 7 weeks is calculate?

What is a related link?

This sounds like the opposite of what Crovella did, i.e. Crovella say the abnormal events are likely to show up better in the less important principal axes.

Is this evenjt detection doe by plateau or what?

Not sure what you are driving at here. We are not defining networks, we monitor existing networks. Coming up with a comprehensive model for network diagnostics seems like a very valuable thing and should be true of any network diagnostics model we come up with. I think you are questioning the appropriateness of  PCA in which case you may need to say why.

I think you should stick to node or host unless you explicity define the difference (i.e. host = monitor, node = montored).  You may want to introduce  some other  way of distinguishing monitor from monitores, e.g. source/target, monitor/remote

Do you want to say something about similar time window/period

What is the score, needs to be defined.

I think you mean monitored here