# Internet Performance to Africa

R. Les Cottrell*, Enrique Canessa+

* Stanford Linear Accelerator Center, 2575 Sand Hill Road, Menlo Park, CA 94025, USA; +The Abdus Salam International Centre for Theoretical Physics – ICTP; P.O.Box 586 - 34100 Trieste, Italy

cottrell@slac.stanford.edu, canessa@ictp.trieste.it

### Abstract

{Enrique can you have a stab at this}

## Introduction

{Enrique this is your section}

## Methodology/setup

The methodology employed by PingER is described in a companion paper [jerrod]. For the results in this paper we utilized monitoring hosts at CERN in Geneva Switzerland, SLAC near San Francisco California, TRIUMF in Vancouver Canada, and the University of Wisconsin in Madison Wisconsin. The use of multiple monitoring hosts enabled us to ensure there were no pathologies associated with a given monitoring host and also to enable comparisons with performance from different parts of the world.

{Probably could extend this to say something about the 1st Round Table and the impetus we got from that, also about the formal collaboration (MOU) between SLAC & eJDS, Enrique can you assist here} To obtain remote hosts to monitor at remote sites in Africa, we found contacts at the sites by sending emails to colleagues especially in the International Committee for Future Accelerators (ICFA) and the electronic Journal Distribution System at the Abdus Salam International Center for Theoretical Physics in Trieste (ICTP) [ejds]. All of these groups are actively working on trying to bridge the Digital Divide gap and so were most helpful. Once we had potential contacts we sent email to them explaining our purpose, our needs, and the possible impact on the network and hosts at the site. Sometimes these emails resulted in further referrals, and/or required extended explanations. Once we had a host to monitor, we then checked that the host was accessible to pings and then entered it into the relevant PingER databases. Typically about 75% of the contacts eventually resulted in a remote host to monitor successfully. Sometimes it took many months to conclude agreements. In some cases pings were blocked and were outside the control of the remote site personnel (e.g. if a service provider blocked the pings).

Currently we monitor hosts in: the Biotechnology and Nuclear Agric. Research Institute of the Ghana Atomic Energy Commission in Accra Ghana, Obafemo Awolowo University in Ife-Ife Nigeria, Makrere University of Kampala Uganda, Schoolnet in Windhoek Namibia, the University of Cape Town S. Africa, Mussel Bay South Africa and Johannesburg S. Africa. All the hosts, apart from the last two are at Academic and Research (A&R) sites. The last two are commercial sites that we obtained through TomWare.

## Results

We used traceroute to find the routes from SLAC to the remote hosts. The route to: Ghana used UUNET and Satworks as the carriers; Namibia used UUNET and xantic; Nigeria used TELIANET and New Skies; Uganda used Level(3) and globalconnex; and South Africa used C&W and Telkom S. Africa (Mossul bay), UUNET and Internet Africa (Johannesburg), and CAIS and Telkom S. Africa (University of Cape Town).

The average monthly Round Trip Times (RTT) to the various remote hosts in Africa from the monitoring sites in N. America and Europe are shown in Fig. 1. It is seen that for a given remote host there is little difference between the monitoring sites. This may indicate that the common bottleneck in most cases is closely associated with the remote site. It is also seen that the routes to Ghana, Nigeria and Uganda have RTTs of over 600ms. and thus probably include a satellite hop.

The losses averaged over a day from SLAC to various remote hosts in Africa are seen in Fig.2 from the middle of July 2003 to the middle of September 2003. A noticeable step change in the losses to Ghana is seen starting around August 18. This does not appear to be due to ping rate limiting. The effects appear to vary from hour to hour, though there does not appear to be a strong diurnal pattern. The losses occur on the last two hops in Ghana. This is currently under investigation. Following this step change losses to Ghana are terrible making the link almost unusable. Losses to Nigeria although better are still categorized as bad (> 12%) most of the time. Uganda, Namibia and South Africa on the other hand have monthly average losses of between 1 and 3% (acceptable to poor).

Combining the losses and RTTs using the Mathis formula for deriving the maximum TCP throughput [mathis], i.e. Derived throughput ~ MSS/(RTT*sqrt(loss)) and plotting the monthly averages from July though September 2003 for monitoring hosts in N. America and Europe to hosts in Africa yields Fig. 3. It can be seen that derived throughput is best to S. Africa, followed by Uganda and Nigeria with Ghana the lowest. There is over an order of magnitude difference between S. Africa and Ghana. The derived throughput for Nigeria is close to that of the so-called broadband DSL and cable to the home in the U.S., and for Ghana the derived throughput is close to that for a dial up modem. The solid line through the Uganda points is a fit to an exponential to help guide the eye. It appears that the performance for Cape Town, and Uganda is improving while Ghana and Nigeria are holding steady or getting worse.

Conclusions

{Mention poor state of Ghana (maybe re-mention comparison to dial up modem) and Nigeria, order of magnitude difference between some countries, improvements for Uganda and S. Africa, need to add more countries and site in existing countries (to avoid anomalies), the diversity of routes and providers even within S. Africa, compare to S. America or Southern FSU republics where AMPATH and Virtual Silk Road are providing connectivity for several countries. Maybe also mention the difficulty of getting contacts and hosts to monitor in sites/countries with very poor infrastructure where this topic is not high on people’s agenda}.

## Acknowledgements

{This needs work, the current text is stolen from another paper} This work would not be possible without the help of volunteer contacts at the remote sites, the maintainers of the monitoring sites, Jerrod Williams and Connie Logg of SLAC, and Maxim Grigoriev of FNAL. We would also like to thank the members of the ICFA-SCIC and the ICTP/eJDS people for providing contacts in many countries, as well as many suggestions on ways to analyze and report on the data.

## References

{This needs to be finished when we have all the references cited}

[1] “Electronic Journals Delivery Service”, available at http://www.ejds.org/

[2] W. Matthews & R. L. Cottrell, “The PingER Project: Active Internet Performance Monitoring for the HENP Community”, IEEE Communications Magazine, May 2000.

[3] J. Williams & R. L. Cottrell, “PingER Methodology”, ICTP/eJDS Round Table: Developing Countries Accesss to Scientific Knowledge, October 2003

[4] M. Mathis, J. Semke, J. Mahdavi, T. Ott, "The Macroscopic Behavior of the TCP Congestion Avoidance Algorithm", Computer Communication Review, volume 27, number 3, pp. 67-82, July 1997

[5] “AMPATH: The AmericasPATH Network”, available at http://www.ampath.fiu.edu/

[6] “Synack”, available at http://www-iepm.slac.stanford.edu/tools/synack/

[7] “UN Human Development Reports”, available at http://www.undp.org/hdr2003/

[8] “Network Readiness Index”, available at http://www.weforum.org/pdf/Global_Competitiveness_Reports/Reports/GITR_2002_2003/GITR_Rankings.pdf

Please note that the paper is to be a maximum of four (4) pages, including text, tables, figures and acknowledgements!

# Text boxes

Figure 2: Losses from SLAC to African countries Jul-Sep 2003

Figure 1: RTTs from N. America and European monitoring hosts to remote hosts in various African countries

Figure 3: Derived throughput from N. America and Europe to some African countries