# PingER Methodology

# Abstract

# Purpose/Why/Rationale

## Simple Low impact, easy to understand (critical for DD)

### No software/hardware for remote hosts (ubiquitous ping) to install/configure/maintain

### Low network traffic, minimize impact on low performance links

# PingER Methodology

## Architecture

### Figure, hierarchical, monitor site choose own, beacons

## Methodology

### Measurement engine (ref IEEE)

#### From remote hosts database, each 30 mins

#### Prime, 10*100B, 10*1000B by default sites dB

#### Record loss, RTT

#### Derive throughput, jitter, unreachability …

### Gathering & archiving

### Analysis, presentation, tabular, graphical, aggregations (regions, groups), drill down, data selection, quality, metrics

### Coverage

## Visualization

### Pingtable

### Table

### Graphs, FNAL

### Download in tsv, roll your own eg Excel

# Uses & examples

## Indicate need for upgrade, present to policy makers,  and see the effects

### RAL, upgrade effects, constant need for upgardes

### BINP, show need, present, get funding do upgrade ensure it fixes problem

### Comparing neighboring sites/countries to see best and indicate what is achievable, e.g. Israel vs rest of Mid East

## Trouble shoot, e.g. peering changes, router problems, provide quantitative information and timing to ISPs

### DESY

## Choosing an ISP

# Effort & Challenges

## Ongoing effort

### Remote sites (~0%) very little, contact, keep host running, and accessible, respond to questions from central site

### Monitor site (few % FTE): initial install & configure, create and update remote host tables, ensure data is accessible, respond to central site admins

### Archive and central admin (20% FTE): contact monitoring sites whose data is inaccessible, look for pathologies (host disappears, does not respond, rate limiting), contact responsible people and follow up

### Future work if funded

## Ping blocking/rate limiting

### Blocking vs rate limiting

### Signatures: step function increase, close by sites v. different losses, synack vs ping

### Examples

# Conclusions

## Valuable simple, light-weight tool for e2e active Internet performance monitoring

## Provides quantitative historical and near-real time information

## Used for trouble shooting, setting expectations, identify needed upgrades, choosing a providers, present to policy makers and funding bodies

## Effects of projects such as Silk Road, AMPATH, Global Crossing can be very encouraging