Integrating the Network as an Actively Managed Resource: Ultralight, US LHCNet, and Lessons Learned from the SC|05 Bandwidth Challenge

Harvey Newman1, Dimitri Bourilkov2, Julian Bunn, Richard Cavanaugh2, Iosif Legrand1, Shawn McKee3,  Dan Nae1, Sylvain Ravot1, Frank van Lingen1, Yang Xia1, 4William Johnston, 5Don Petravick, 5Matt Crawford, 6Les Cottrell, 6Yee-Ting Li, 7David Foster

1California Institute of Technology, 1200 E. California Blvd. Pasadena,CA  91125, USA

Email:newman,@hep.caltech.edu, {julian.bunn, fvlingen, yxia}@caltech.edu,

{iosif.legrand,dan.nae,sylvain.ravot}@cern.ch

2University of Florida, Department of Physics, Gainesville, FL 32611-8440, USA

Email: {bourilkov, cavanaug }@phys.ufl.edu

3University of Michigan, 2477 Randall Laboratory,Ann Arbor, MI 48109-1120, USA

Email: smckee@umich.edu

4 ESnet, 1 Cyclotron Rd., MS 50B-2239, Berkeley, CA, 94720, USA

Email: wej@es.net

5Fermilab, PO Box 500, Batavia 60510, USA

Email: {petravick@fnal.gov, crawdad@fnal.gov}

6SLAC, 2575 Sand Hill Road, Menlo Park, CA 940251, USA

Email : {cottrell, ytl}@slac.stanford.edu

7CERN, CH-1211 Genève 23, Switzerland

Email : david.foster@cern.ch

Keywords: global network management, network monitoring, network protocols

### Introduction

The High Energy Physics (HEP) community engaged in CERN’s Large Hadron Collider (LHC, see lhc.web.cern.ch/lhc/) is preparing to conduct a new round of experiments to probe the fundamental nature of matter and space-time, and to understand the composition and early history of the universe. The LHC is expected to begin operations in 2007. The associated LHC experiments face unprecedented engineering challenges due to the volume and complexity of the experimental data, and the need for collaboration among scientists located around the world. The massive datasets which will be acquired, processed, distributed and analyzed are expected to grow to the 100 Petabyte level and beyond by 2010. Distribution of these datasets will require aggregate network speeds of in the 10-100 gigabits per second (Gbps) range in the early phase of LHC operation. The data volumes are expected to rise to the Exabyte range, and the corresponding network throughputs to approach the 1 Terabit/sec range, by approximately 2015.

In response to the network challenges, US LHCNet (http://lhcnet.caltech.edu/) co-operated and managed by Caltech and CERN, is developing and deploying transatlantic wide area network links, points of presence at Starlight (http://www.startap.net/starlight/), CERN, and MANLAN (http://networks.internet2.edu/manlan/), and the necessary high performance software infrastructure needed to support networking on this scale.

A 10 Gbps triangle among the three points of presence was deployed in November 2005, with the intention to add one wavelength to this triangle each year (contingent on sufficient funds from the  Department of Energy), so that 60-80 Gbps of network bandwidth will interconnect the US Tier1 and Tier2 centers to CERN by 2007-8. Production network connections to the Tier1 centers at Fermilab and BNL are being handled by ESnet (http://www.es.net/), in cooperation with US LHCNet.

### UltraLight

The Grid-based infrastructures developed by collaborations in the US, Europe and Asia such as EGEE (Enabling Grids for E-sciencE: http://egee-intranet.web.cern.ch/egee-intranet/gateway.html), OSG (Open Science Grid: http://www.opensciencegrid.org/) and Grid3 (http://www.ivdgl.org/grid2003/) provide massive computing and storage resources. However, efficient use of these resources is hampered by the treatment of the interconnecting network as an external, passive, and largely unmanaged resource, creating the risk of a “network traffic jam”, where we deal with the management of the limited CPU and storage resources but have neglected the network as the “third resource”. The US NSF-funded UltraLight project, working side-by-side with US LHCNet, ESnet, and partner projects in the US, Europe and Asia, aims to overcome these limitations by treating the network as an end-to-end monitored and managed resource along with storage and computing. The consortium (see sidebar) deployed the UltraLight hybrid packet- and circuit-switched network infrastructure which employs both “ultrascale” protocols such as FAST [2], and the dynamic creation of optical paths for efficient fair sharing on long range networks in the 10 Gbps range (see Figure 1).

Figure 1. A schematic view of the initial Ultralight setup and connections to other major networks and Caltech's WAN in Lab (http://wil.cs.caltech.edu)

The main goals of Ultralight are: (1) to develop and deploy prototype global services which broaden existing Grid computing systems by promoting the network as an actively managed component. (2) Integrate and test UltraLight in Grid-based physics production and analysis systems currently under development for LHC experiments. (3) Engineer and operate a trans- and intercontinental optical network testbed, including high-speed data caches and computing clusters.

### SC|05 Bandwidth Challenge

Using this state of the art network, the Ultralight consortium participated (and won) the Bandwidth Challenge at SC2005 (BWC). The BWC provides an ideal environment for dedicated access to network resources for a limited amount of time and stress testing both hardware and software on a global scale. Within 2 hours an aggregate of 95.37 TB (Terabyte) was transferred, with sustained transfer rates ranging from 90 Gbps to 150 Gbps and a measured peak of 151 Gbps (see Figure 2). During the whole day (24 hours) on which the bandwidth challenge took place approximately 475 TB where transferred. This number (475 TB) is lower than the team was capable of as they did not always have exclusive access to waves, outside the bandwidth challenge time slot. Multiplying the 2 hours where 95.37 TB was transferred, times 12 (to represent a whole day) you get approximately 1.1 PB (Petabyte). Such heavy load on the system exposed stability limits of server and network interfaces (and heating) under heavy loads. It also enabled the team to effectively utilize 10GE and 1GE connected systems to drive 10 gigabit wavelengths in both directions.

The extraordinary data transport rates were made possible in part through the use of the FAST TCP protocol as well as new data transport applications developed at Fermilab, SLAC, DESY and INFN/Padova (dCache/SRM [6], BBCP [3] and Xrootd [4]) and an optimized Linux kernel developed at Michigan. The SC|05 BWC and preparations leading up to it, resulted in an optimized Linux (2.6.12 + FAST + NFSv4) kernel for data transport; after 7 full kernel-build cycles in 4 days. The BWC also led to a deeper understanding of the applications. BBCP, matches the performance of iperf under some conditions. The BBCP rate from 20 Caltech nodes to Storcloud storage facility  (http://sc05.supercomputing.org/initiatives/storcloud.php) was around 320~350MB/s for each node and could get as high as 380MB/s for some nodes. The aggregate sustained rate for 20 nodes was over 6GB/s. SLAC recorded about 3.2 TByte of data to StorCloud in 1649 files at the same time as it transferred over 18 TBytes in 257,913 files via Xrootd over the network between SLAC and SC|05.

During the challenge MonALISA [1] monitored and displayed the real-time data for all the network links, storage resources and scientific applications used in the demonstration. Such an end-to-end monitoring capability enabled quick identification of problems. Most problems required human intervention, but in the near future some of these problems will be dealt with by autonomous applications that have a global view of the system and handle problems such as restarting a large dataset transfer, resetting applications or hardware, rerouting data streams, etc… .

Figure 2. Average of more than 100 Gbps for 3 hours during the bandwidth challenge. (picture generated using MonALISA [1] )

Such autonomous behavior will further optimize the (network) resource usage and increase bandwidth efficiency. A first step towards autonomous applications has been the development of LISA (Localhost Information Service Agent). This application helps in optimizing other applications by means of monitoring services.

### Conclusions

While the SC|05 demonstration required a major effort by the teams involved and their sponsors, in partnership with major research and education network organizations in the U.S., Europe, Latin America and Asia Pacific, it is expected that networking on this scale in support of the largest science projects (such as the LHC), will be commonplace within the next three to five years.  By demonstrating that many 10 Gbps wavelengths can be used efficiently over continental and transoceanic distances (often in both directions simultaneously), the HEP team showed that this vision of a worldwide dynamic Grid supporting many Terabyte or larger data transactions is feasible and that issues such as End-2-End monitoring and management need to be addressed in an integrated orchestrated manner between CPU, storage and network resources.

### Acknowledgements

This work is partly supported by the Department of Energy grants: DE-FC02-01ER25459, DE-FG02-92-ER40701, DE-AC02-76CH03000 (Particle Physics DataGrid project), DE-FG02-04ER-25613 (Lambda Station project), DE-AC02-76SF00515 (Terapaths project) and DE-FG02-05ER41359 (LHCnet project), and by the National Science Foundation grants:  PHY-0122557, PHY-0427110 (Ultralight project) , ANI-0113425, EIA-0303620(WAN in Lab project). We would also like to acknowledge the generous support of our many sponsors and contributors (http://ultralight.org/web-site/sc05/html/contributors.html). Any opinions, findings, conclusions or recommendations expressed in this material are those of the authors and do not necessarily reflect the views of the Department of Energy or the National Science Foundation.

### References

- H.B. Newman, I.C. Legrand, P. Galvez, R. Voicu, C. Cirstoiu "Monalisa : A Distributed Monitoring Service Architecture." In proceedings of Computing for High Energy Physics (CHEP), Paper ID: MOET001, La Jolla, California, June 2003.. (see also: http://monalisa.caltech.edu/)

- Cheng Jin, David X. Wei and Steven H. Low. “FAST TCP: motivation, architecture, algorithms, performance”, Proceedings of the IEEE Infocom, Hong Kong, March 2004.  (see also: http://netlab.caltech.edu/FAST)

- A. Hanushevsky, A. Trunov, Les Cottrell, “Peer-to-Peer Computing for Secure High Performance Data Copying”, in proceedings of Computing for High Energy Physics (CHEP), Beijing, China, September 2001

- A. Hanushevsky, A. Dorigo, F. Furano, “The Next Generation Root File Server”, In proceedings of Computing for High Energy Physics (CHEP), Paper ID: 328, Interlaken Switzerland, September 2004 (see also: http://xrootd.slac.stanford.edu/)

- H. Newman, J. Bunn, I. Legrand, S. Low, D. Nae, S. Ravot, C. Steenberg, X. Su, M. Thomas, F. van Lingen, Y. Xia, R. Cavanaugh, S. McKee, "The Ultralight project: The Network as an Integrated and Managed Resource for Data Intensive Science", in Computing In Science and Engineering, Special issue on grid computing (part II), November 2005 (see also: http://ultralight.org)

- M. Ernst, P. Fuhrmann, T. Mkrtchyan, J. Bakken, I. Fisk, T. Perelmutov, D. Petravick, “Managed Data Storage and Data Access Services for Data Grids,” Proceedings of Computing for High Energy Physics (CHEP) 2004, Interlaken, Switzerland, September 2004 (see also http://www.dcache.org/)

### Vitae

Harvey Newman, the UltraLight project’s principal investigator, is a professor of physics at the California Institute of Technology (Caltech) and the board chair of the US CMS collaboration. His research interests in­clude elementary particle physics, global distributed grid systems, and intercontinental networks for data-intensive sciences. He co-led the physics collaboration that discovered the gluon in 1979 and was part of the NSFNet Technical Advisory Group in 1986. He’s led the Caltech team that has won 11 Internet2 Land Speed records since 2003. Newman has an ScD in physics from MIT. Contact him at newman@hep. caltech.edu.

Richard Cavanaugh, UltraLight’s project manager, is a research physicist at the University of Florida, where he is a member of the CMS Collaboration and several grid computing projects. His research interests include establishing experimental signatures for theories pre­dicting cold dark matter candidates that might be pro­duced at the Large Hadron Collider, and effective co-utilization of resources (computational, storage, networking) for high-energy physics data analysis in a grid environment accounting for differential policies within and across multiple large virtual organizations. Cavanaugh has a PhD in physics from Florida State University. Contact him at cavanaug@phys.ufl.edu.

Julian James Bunn is a faculty associate and senior sci­entist at the Center for Advanced Computational Re­search at Caltech. His research interests include Web-based information systems, petabyte-scale distributed databases, grid middleware, high-performance computing and networking, object-oriented technology, and biological systems modeling. Bunn has a PhD in physics from the Universities of Sheffield and Manchester in England. Contact him at julian.bunn@caltech.edu.

Iosif Legrand is a senior software engineer at Caltech, Division of Physics, Mathematics, and Astronomy. His research interests include distributed network services, monitoring systems, and grid-related activities. Legrand has a PhD in physics from the National Institute for Physics, Bucharest. Contact him at iosif. legrand@cern.ch.

Dan Nae is a network engineer at Caltech. His research interests include network protocols, control and moni­toring. Nae has an MSc in computer science from Politehnica University of Bucharest. Contact him at dan.nae@cern.ch.

Sylvain Ravot is a network engineer at Caltech, Division of Physics, Mathematics, and Astronomy, and is currently based at CERN in Geneva. His research interests include protocols for fast long-distance networks, high performance networking, network monitoring. Ravot has a degree in communication systems from the Swiss Federal Institute of Technology (Lausanne). Contact him at sylvain.ravot@cern.ch.

Frank van Lingen is a scientific software engineer with the High Energy Physics group at Caltech. His research interests include distributed systems, high-performance computing, graphs in distributed systems, and software design. Van Lingen has a PhD in computer science from the Eindhoven University of Technology, the Netherlands. Contact him at fvlingen@caltech.edu.

Yang Xia is a network engineer at Caltech, Division of Physics, Mathematics and Astronomy. His research interests include network and data transfer behavior over high bandwidth/latency networks. Xia has MS degrees in electrical engineering and physics from the Univer­sity of Missouri. Contact him at yxia@caltech.edu.

Shawn McKee is a high-energy astrophysicist in the University of Michigan Physics Department. His research interests include particle astrophysics, neutrino physics, high-energy physics, and observational cosmology. McKee has a PhD in physics from the University of Michigan. Contact him at smckee@umich.edu.

Dimitri Bourilkov is coordinator of the Ultralight User community workgroup and a research physicist at the University of Florida. His research interests are centered on searches for extra dimensions and compositeness with high mass lepton pairs from LEP to the LHC and on development of collaborative systems for data analysis and software development in distributed and grid environments. Bourilkov has a PhD in physics from the Institute for Nuclear Research and Nuclear Energy, Sofia. Contact him at bourilkov@phys.ufl.edu.

William Johnston is a Senior Scientist and manager of the US Dept. of Energy, Energy Sciences Network (ESnet) in the Information Technologies and Services Division of the Computing Sciences Directorate of Lawrence Berkeley National Laboratory. His research interests include high-speed, wide area network based, distributed systems, widely distributed computational and data "Grids," and use of the global Internet to enable remote access to scientific, analytical, and medical instrumentation. Johnston has a Masters Degree in Mathematics and Physics from San Francisco State University. Contact him at wej@es.net.

Don Petravick is the head of the Computation and Communications Fabric department in the Fermilab Computing Division. He is interested in data systems for globally distributed, data intensive science. Contact him at petravick@fnal.gov.

Matt Crawford is the leader of the Wide Area Systems group in the Fermilab Computing Division. His current interests include optical networking, data transfer applications and application-to-network interfaces. He has a PhD in physics from the University of Chicago. Contact him at crawdad@fnal.gov.

Les Cottrell is the assistant director of SLAC's Scientific Comnputing and Computer Services group and leader of the Internet End-to-end Performance Monitoring  (IEPM) team at SLAC. His research interests include monitoring, analyzing Internet performance and high performance networking. Cottrell has a PhD from the University of Manchester, England. Contact him at cottrell@slac.stanford.edu.

Yee-Ting Li is a network researcher at SLAC. His interests include high performance networks and protocols. Li has a PhD from University College London. Contact him at ytl@slac.stanford.edu.

David Foster is head of the networking and communications group at CERN. He is also the Chief Technology Officer of the LHC computing Grid Project He has more than 20 years of experience in running large production infrastructures for the needs of the scientific community. In addition to a PhD in physics he holds an MBA, both from the University of Durham, and is a fellow of the Institute of Physics and a Member of the Institute of Chartered Managers. Contact him at david.foster@cern.ch.

# Text boxes

Ultralight Consortium Member Organizations: The US National Science Foundation funds the Ultralight project which is based on a strong partnership between the following organizations:

Caltech

University of Florida

University of Michigan

SLAC

Fermilab

CERN

Universidade do Estado do Rio de Janeiro

Internet2

University of Sao Paulo