## Slide 1: How cell phones work
Les Cottrell – SLAC
University of Helwan / Egypt, Sept 18 – Oct 3, 2010
Partially funded by DOE/MICS Field Work Proposal on Internet End-to-end Performance Monitoring (IEPM), also supported by IUPAP
Cell-phones

## Slide 2: Outline
Caveat
How cell phones work
History of technologies
Cell phones components
Power
Coverage
Growth
Concerns
Benefits

## Slide 3: Not covering other mobile devices
Cordless phones, CB radios, pagers, car phones, Bluetooth etc.
Iridium: catastrophes (Haiti), hard to reach places: expeditions, Arctic …
ATT Terrestar hybrid cell & satellite switches to satellite when out of range, covers US, looks like Blackberry, not cheap $799 + $5/month on top of regular voice & data. Calls are $0.65/min. See http://www.pcworld.com/article/172944/terrestar_satellite_phone_coming_to_atandt.html

## Slide 4: Base Stations
City divided up into cells size ~10 sq miles.
Each cell has a base station consisting of:
  a tower (sometimes disguised), with ladder, lightening arrester
  antennas, facing 3 sectors,
  a small building containing radio equipment, UPS, cooling etc.
  Access to power
  a GPS antenna
  lots of cables
  An uplink to carry signals
For disguising towers see:
http://www.networkworld.com/slideshows/2009/092509-cell-tower.html
What is the GPS antenna for?

## Slide 5: Architecture
Since cell-phones & base-stations use low power transmitters so the same frequency can be re-used in non-adjacent cells
  Cells typically 1-2 miles apart in urban areas, by reducing power
  Max distance: tall mast, flat terrain ~ 20miles, can reduce to 3miles
  _
Single cell uses 1/7 of frequencies allocated to carrier, blue cells can re-use same frequencies since no overlap
  Cells reserve part of available bandwidth for emergency calls
Tower cost with permits, construction etc. $150-400K, 9mos – 3years (with permits), but many people can use a single tower so costs are low
What are benefits of low frequencies (e.g. 850MHz vs 1800MHz)?
Notes: Towers: cost $120-500K, 9mos to 3 years (incl permits & construction), 80’-400’, 20 people
Frequencies : low is good: potentially 2-3 times more cell towers for same coverage.
FCC to free more WiFi bandwidth using the no longer used analog TV channels now they moved to digital.
While the increased availability of WiFi in rural areas is one obvious application for this additional bandwidth, other possibilities include smart grids for electric distribution, remote patient management for hospitals, and larger corporate wireless networks.

## Slide 6: Cheaper
OpenBTS = open-source Unix application that presents a GSM air interface to standard GSM handset
  uses the Asterisk® software PBX to connect calls.
The combination of the ubiquitous GSM air interface with VoIP backhaul could form the basis of a new type of cellular network that could be deployed and operated at substantially lower cost than existing technologies in greenfields in the developing world.
  installed and operated at about 1/10 the cost of current technologies,
  compatible with most of the handsets that are already in the market.
  Range depends on antenna
Few metres range
Desert
http://openbts.sourceforge.net/

## Slide 7: How they work
Each carrier in each city runs a Mobile Telephone Switching Office (MTSO) that controls Base Stations and handles phone connections
MTSO
BDA

## Slide 8: Connecting
At power-on phone listens on the control channel for SID (5 digit number unique to each carrier)
Phone compares with SID in phone, transmits a registration request to MTSO which tracks phone location in a database
When MTSO gets calls looks in database to see which cell phone is in.
MTSO picks frequency pair & tells phone and base station over control channel
Base station & phone connect up on freq pair

## Slide 9: Moving from Cell to Cell
MTSO

## Slide 10
MTSO

## Slide 11
MTSO

## Slide 12
MTSO

## Slide 13
MTSO

## Slide 14
MTSO

## Slide 15
If the SID on the control channel does not match the SID on the phone then phone knows it is roaming
The MTSO of the cell you are roaming in contacts the MTSO of your home system
The home MTSO confirms the phone’s SID is OK
The home MTSO verifies SID is OK to roaming MTSO
All happens within seconds
Roaming can be expensive.
If roaming internationally may need phone with supporting multiple technologies
Roaming

## Slide 16: Analog phones (1st gen)
1983: Advanced Mobile Phone System (AMPS) by FCC and first used in Chicago
Use 824-894MHz frequency range
Each carrier is assigned 832 frequencies
  790 for voice and 42 for data
  Voice channel 30kHz wide (quality equivalent to wired voice)
  Each channel has 2 frequencies (xmt & rcv) separated by 45 MHz
    i.e. 395 voice channels and 21 control channels

## Slide 17: Digital 2G technology
Adds compression, fit more channels into given bandwidth (3-10 times more)
  Frequency division multiple access (FDMA)
    Each call uses a separate frequency, inefficient, mainly used in analog
  Time division multiple access (TDMA)
    Each call uses a certain portion of time on a given frequency, 3 times capacity of analog. This is used by GSM (see later).
  Code division multiple access (CDMA)
    Uses a unique code to each call and spreads it over the available frequencies, It uses GPS for timing

## Slide 18: Global System for Mobile communications (GSM)
Implements TDMA
Has encryption for security
Uses 900MHz and 1800Mhz in Europe, Australia and much of Asia and Africa,
  In other countries switch SIM card
  Lower frequency=longer range, use in rural areas
Unfortunately uses 850MHz and 1900MHz in US
  Travel to Europe etc, need tri- or quad band phone
Some providers lock the phone to their service
  Unlocking requires a special key
  Data rates are typically modem (< 140kbits/sec(GPRS aka 2.5G), typically <=56kbps) based

## Slide 19: 3G (Third Generation)
Meant for multimedia phones = Smartphones
Increased bandwidth and transfer rates, adds data
  Up to 3Mbps (15 sec for 3 min song) cf 144kbps for 2G
  Accommodate: web applications, audio & video files
Several cellular access protocols
  EDGE (Enhanced Data Rates for GSM Evolution aka 2.75G) 3*capacity & performance of GSM/GPRS, easy upgrade from 2G GSM, < 1 Mbps
  CDMA based on 2G Code Division Multiple Access
  WCDMA (UMTS) wideband CDMA < 21Mbit/s
  TD-SCDMA – Time-division Synchronous CDMA
  HSDPA (High Speed Downlink Packet Access – aka 3.5G) based on UMTS & backward compatible <21.0Mbits/s
  HSPA+ < 42Mbits/s

## Slide 20: 4G
4G mobile technology is the name given to the next generation of mobile devices such as cell phones. It became available from at least one provider in several parts of the US in 2009. There is not yet an agreed industry standard for what constitutes 4G mobile, so for now it is merely a marketing term.
Two contenders WiMAX and LTE (long term evolution)
  ~ 100Mbps down, 50Mbps up on 20MHz channel
  WiMax began testing in 2008 (Baltimore), 80 cities by end 2010, only 10Mbps
  LTE testing 14 Dec 2009 (Stockholm, Oslo)
Increases data speeds, enhanced security, HDTV, mobile TV, intended for Internet use on computers too, IP packet switching only, IPv6

## Slide 21: Inside a Digital cell phone
battery
speaker
keyboard
microphone
LCD display
microprocessor
Flash memory removed
One of the most intricate devices used daily
  Compression take lot of compute power (MIPS), A-to-Ds, digital signal processor (DSP), radio (hundreds of channels), microprocessor, ROM, flash memory, power mgmt, clock
  Now smartphones
Antenna
backup battery
for clock

## Slide 22: Phone power
Many manufactures have agreed on standard (micro-USB) for charging phones. So no longer need a charger with each phone.
November 2008 the top five mobile phone manufacturers Nokia, Samsung, LG Electronics, Sony Ericsson and Motorola set up a star rating system to rate the efficiency of their chargers in the no-load condition.
Formerly, the most common form of mobile phone batteries were nickel metal-hydride, as they have a low size and weight.
  lithium ion batteries are sometimes used, as they are lighter and do not have the voltage depression that nickel metal-hydride batteries do.
  Many mobile phone manufacturers have now switched to using lithium-polymer batteries as opposed to the older Lithium-Ion, the main advantages of this being even lower weight and the possibility to make the battery a shape other than strict cuboid.
  Mobile phone manufacturers have been experimenting with alternative power sources, including solar cells.
The main requirements for the cpus is low power, the main contending designs are ARM/Eagle (Qualcom/Snapdragon, Apple/A4, Samsung/Hummingbird, TI) and Intel/ATOM.
Notes: Processors see http://www.rethink-wireless.com/2010/08/10/ti-flies-ahead-arm-pack-eagle-deal.htm
ARM=Acorn RISC Machine => Advanced RISC Machine

## Slide 23: Top carriers in subscribers http://en.wikipedia.org/wiki/List_of_mobile_network_operators
1. China Mobile – China (540M)
2. Vodafone – UK (427M)
3. Telefonica/Movistar/O2 - Spain (206M)
4. America Movil – Mexico (203M)
5. Orange (189M)
6. Telenor (174M)
7. Bharti Airtel – India (185M)
8. T-Mobile – Germany (150.9M)
9. China Unicom – China (147M)
10. Orascom Telecom/WIND – Egypt (120M)
11. MTN – South Africa (116M)
12. TelaSonera – Sweden (102M)
13. Reliance – India (102M)
14. Etisalat – UAE (100M)
15. MTS – Russia (102M)
16, 17 Verizon, AT&T – USA (92.8M, 87M)
Notes: http://en.wikipedia.org/wiki/List_of_mobile_network_operators -

## Slide 24: Coverage depends on provider
Verizon
AT&T
Sprint
Notes: Grey is roaming

## Slide 25: Coverage and bars etc.
BARS have a little to do with signal strength, there are no industry standards.
The main thing is the networks access level.
  Y (in dBm) = 10 *( log10(power (in mWatts))), 1milliwatt=0dBm, 1W=30dBm, 1 nanowatt= -60dBm etc.
  The –dBm can vary from minute to minute by -10dB or more. This may depend on trafffic, congestion, technology, moving bodies, how tightly it is held in the hand (24.6dB to 19dB) etc.
Record minimums with clear audio are: -104dBm - Cingular (GSM) -111dBm - Cingular (TDMA) -109dBm - T-Mobile With garbled or no audio, my record minimums while holding a call are: (These calls did NOT drop but audio faded for a few seconds) -113dBm - Cingular (GSM) -113dBm - Cingular (TDMA) -112dBm - T-Mobile It really depends on the area, codec used, congestion, noise, interference, etc. Minimum signal seen while registered to a tower (not in a call): -117dBm - Cingular (GSM) -113dBm - Cingular (TDMA) -115dBm - T-Mobile
For most phones (not Apple) with 5 bars, each bar is worth 5dBm. So that means: 0 bars: No signal to -100dBm (<-113dBm) 1 bar: -100dBm to -95dBm (-113 dBm to -107 dBm) 2 bars: -95dBm to -90dBm (-107 dBm to -103 dBm) 3 bars: -90dBm to -85dBm (-103 dBm to -101 dBm) 4 bars: -85dBm to -80dBm (-101 dBm to -91 dBm) 5 bars: -80dBm or stronger (-91 dBm to -51 dBm)
Regardless of the max number of bars in the phone, usually the most bars is reached at around -80dBm, 10pW.
Notes: See http://en.wikipedia.org/wiki/DBm for definition of -dBmW
Most of the information is from you can see the bars display freeze at 2 or 3 bars even if the signal is lost. This usually happens because the phone is scanning.
http://forums.wirelessadvisor.com/general-wireless-discussion/11301-signal-strength-db-vs-bars.html
It is important to know that the bars display doesn't get updated as quick as the dBm reading in the Test Field screens, so it doesn't always match.
Apple iPhone bars to –dB loss from http://www.boygeniusreport.com/2010/06/30/iphone-4-bars-to-signal-strength-mapped-antenna-issue-partially-explained/

## Slide 26: In Building Coverage
Pick up signal outside with antenna (omni or directional), carry to master unit (fibre or copper coax, usually copper), boost signal then redistribute to internal antenna
  Building Distribution Amplifiers
    Multi carrier, business solution, several to tens of $K
    Can interfere with carriers cell tower, may need agreement
  Micro (2km), Pico (200meters),
  Femto (10meters)-cells
    Cheap, but single carrier, good for home, needs Internet (by passes cell phone towers)

## Slide 27: Growth
Mobile telecommunications connections worldwide reached five billion in the first week of July on growth in India and China, and could triple by 2016, PRTM Management Consultants said.
Revenue will “probably grow 20 percent to 30 percent in the same time,” Ameet Shah, a consultant for PRTM, said from London in a telephone interview. The current revenue figure is about US$900 billion, according to researcher The Mobile World.
Operators must change their operating models and may need to merge to survive, Shah said. Instead of concentrating on “high value, high price and low volume” they must focus on “immense scale, low value and low prices,” he said. Some markets have grown to 150%-200% penetration relative to their populations. More penetration than Internet.
In the US there is a growing demand for increased bandwidth for newer services (see below), however 4G upgrade is very expensive. It may only be affordable by companies like Verizon and AT&T and could drain money for wireless build-out from standard services (e.g. wired). In US this could lead to a duopoly since T-Mobile and Sprint may not be able to compete.

## Slide 28: Concerns
Radiation
  Tower:
    Worst case ground level power density 1uW/cm2 or 0.01 W/sq m cf avg energy over entire earth ~ 250W/sq m/day ignoring clouds, i.e. electro magnetic energy from Sun 25K times that of cell phone tower.
  Handset:
    Mainly from antenna, closer to head higher exposure
    So use ear phones and mike
    Measured metric is the Specific Absorption rate (SAR). An SAR of < 1.6 watts/kg of body weight is considered safe by the FCC. The SARs for manufactured phones vary from 0.1 to 1.59 watts/kilogram
Privacy
  Use multilateration based on RTT to towers to discover location of cell phone whether turned on or not
  Remotely turn on microphone of some cell phones and listen to conversations (see http://news.cnet.com/FBI-taps-cell-phone-mic-as-eavesdropping-tool/2100-1029_3-6140191.html)
Consideration
  Lack of attention when driving
  Interrupting others
Notes: See http://www.seas.harvard.edu/courses/es96/spring1997/web_page/health/fccregs.htm
FCC guidelines for radiation emissions from radio frequency transmitters operating at a frequency range of 300KHz - 100GHz are based on ANSI/IEEE C95.1-1992. It includes Maximum Permissible Exposure (MPE) limits for the power density and magnetic and electric field strength from FCC regulated RF transmitters. The guideline also contains limits for the partial body absorption from portable transmitting devices.

## Slide 29: Some Benefits
What no coverage!
From the Economist, Sep 26, 2009
Mobile computing (in future any micro-processor will have a wireless access):
Rent a car check in at the curb
Real time Bus schedules for students
Field workers, mobile workers
Push button access to nurse practitioners
Even warlords may need & protect
Emergencies, reporting fires, accidents
Keeping in touch
  Market prices (fish, crops), weather, crop information
  Family, friends and co-workers etc
Given to victims of domestic violence
Emergencies, reporting fires, accidents
Keeping in touch
From the Economist