| Stored Current Interlock I/O Signals Available on EDM Page |
| --- |
| Parameter | Input/Output of IP470A Module | Logic High | Logic Low | Description | IP470A Module Channel |
| SCI CH A | Input | Enable (Green) | Disable (Red) | Display a green square when this bit is logic high; display a red square when this bit is logic low | TBD |
| SCI CH B | Input | Enable (Green) | Disable (Red) | Display a green square when this bit is logic high; display a red square when this bit is logic low | TBD |
| SCI LTB Stoppers | Input (derived) Note 1. | Enable (Green) | Disable (Red) | Logical “AND” of SCI CH A & SCI CH B. Display a green square when high; red when low. | N/A |
| Reset | Output | Inactive | Low 5 msec. | Pulse low for 5 milliseconds to reset a fault. | TBD |
| DCCT Trip Test | Output | Inactive | Low 6 sec. | Pulse low for 6 seconds to drive a test current through the DCCT. This time should be sufficient to reach the limiting current value of 525 mA. | TBD |
| NPCT Trip Test | Output | Inactive | Low 6 sec. | Pulse low for 6 seconds to drive a test current through the NPCT. This time should be sufficient to reach the limiting current value of 525 mA. | TBD |

Note 1.  This is not an actual input, but is derived from SCI CH A & SCI CH B.  This summary signal exists inside the SCI hardware, but cannot be used because of a logic inversion.  The enabled condition is logic low, which would be indistinguishable from a power loss.  Therefore the request is to provide SCI LTB Stoppers indication in software, if possible.