PEP Master Source Phase Shifter

The PEP phase shifter is made up of 9 of 180 degree 476MHz phase shifters.  The slope near the 5 volt level of a single unit is about 18degrees/volt.  For 8 units this is 144degrees/volt.  This unit should be stable to 0.002 degrees which is 14uV.

The noise contributions seen are as follows:

1 to 5MHz is 2fS = integrated noise of 6uRadians = -105dBc over 4MHz => -171dBc/Hz

100kHz to 1MHz not much increase

10kHz to 100kHz is 12fS => 36uRadians = -89dBc over 100kHz = -139dBc/Hz

540Hz is 9fS-6fS= 7fS = 20uR = -94dBc or -97dBc SSB

420Hz is 13fS-9fS= 9fS = 26uR = -92dBc

300Hz is 25fS-13fS= 21fS = 61uR = -84dBc

180Hz is 60fS-25fS= 54fS = 157uR = -76dBc

Noise sources should be addressed in the following order:

1. 180Hz

2. 300Hz

3. 10kHz to 100kHz

I expect the noise in the above listed frequency ranges to be associated with DC Power supplies and analog electronics.

In reviewing the chassis, the following has been noted:

There is about the same noise level in the lab and in Sector 0, about 0.08 degs p-p.

Bypassing the amplitude section did not change this.

Bypassing the phase shifter section changed reduced this to about 0.03 degs p-p.

Running the phase shifters on batteries still gave the 0.08 deg p-p.

There is about 0.5mV voltage difference between grounds in the chassis.

The control voltage for the phase shifters has a sensitivity of 7mV/deg.

The allowable noise level on this line would be 14uV rms, a fraction of the ground voltages.

Noise measurements - see:

Linac Phase Noise Measurements

August 17, 2004

R. Akre, K. Schaffold

Integrated Noise - Timing Jitter fs rms

Integral end 	5MHz				10kHz

Integral start 	1M	100k	10k	1k		100	10

Master Osc.	9	10	10	10		5	8

PEP Phase		11	13	17	18		60	60

Master Amp	24	27	31	37		68	72

MDL			24	28	31	37		72	76

Sector 30		27	30	33	38		75	82

Scale Factor 575000						Scale Factor 560000

Scale Factor 575000						Scale Factor 560000