Task

- The RF Gun reflects power to the klystron.  Large amounts of reflected power to the klystron can cause phase and amplitude instabilities in a klystron.  Look at pulse shaping as a way to reduce reflected power to the klystron and eliminate the requirement for a 30MW S-Band circulator between the RF Gun and klystron.

- Calculate the reflected power from the RF Gun as a function of  the RF input power pulse.

- Increase the power pulse gradually, so the reflected power stays all the time below 4 MW.

Method

- Calculation of the reflected power is carried out in the frequency domain.

- The frequency domain spectrum of the RF input pulse is obtained by the FFT on the user defined shape of the input pulse in the time domain.

- Next the Reflection Coefficient ( is expressed as a function of the cavity Transfer Function near the resonant frequency.

- Reflected signal is calculated as a product of the Fourier transform of RF input signal and the cavity Reflection Coefficient (.

- Reflected signal is transformed back into the time domain applying the inverse Fourier Transform, IFFT.

- Filling of the cavity – the increase of the cavity electric field is calculated from the input power pulse and parameters of the RF Gun resonator.

- The reflected power and the cavity voltage vs. time are plotted into the same graph.

Theory

- The general expression for (complex) Reflection Coefficient is:

(1)

Zc is the impedance of the “load”, i.e. the resonant cavity, and Zw is the characteristic impedance of the connecting line.

- The impedance of a resonator near its resonant frequency (o is expressed as:

(2)

RSH is the resonator shunt resistance, Ql is the quality factor (including the loading from the external circuits) and detuning (( = ( - (o,  (( « (o. Here ( is the frequency independent variable and (o is the resonant frequency.

- The cavity coupling coefficient ( is defined as ( = RSH/Zw .

Substituting for RSH in (2) and combining (1) and (2), the expression for the Reflection Coefficient in terms of resonator parameters is given

.				(3)

( is cavity filling time constant, ( = Ql/(o.

- The frequency spectrum of the input signal into the cavity is calculated from the shape of the input power pulse as V((() = FFT{√p(t)}.

- The reflected signal in the frequency domain can be directly calculated as

Vrefl((() = V((().(((().					(4)

- The Inverse Fast Fourier Transform, (IFFT), transforms this result back into the time domain,

v(t) = IFFT{ Vrefl((()}. 						(5)

- The reflected power is plotted as a function of time using the square of the v(t).

- The exponential increase of cavity electric field is calculated from the input power pulse, cavity shunt impedance RSH and the cavity time constant (. It rises as (1- e-t/(2.()).

Program/Calculation

- The MATLAB program is used to calculate reflected power and to plot the results.

- User can define the shape of the input power pulse and the other relevant parameters of the RF gun resonator

  - coupling coefficient ( (= 2.1),

  - cavity (unloaded) quality factor Qo (=13369),

  - cavity shunt impedance RSH (=1.65 M().

- The input and reflected power is expressed in MW, the developed cavity voltage signal in MV.

- Program is available and can be tested and used by anyone interested.

Results

- Present MATLAB plots – the results are calculated for the parameters given above.

- The input power pulse has 4 intermediate steps, the height of each step is 25% of the maximum power. The duration, (width), of those steps is 4x, 5x, 5x, 4x of a single interval of the control clock step, 8.4 ns.

References

1)Zenghai Li: Reflection Isolator using a Hybrid and a Dummy Cavity for the LCLS RF Gun., SLAC/LCLC, (2005)

2) Jens Knobloch: Basic Concepts of Measurements Made on Superconducting RF Cavities., SRF note, #910927-07, (1991)

3) Tom Hays: Cavity Analysis By Reflection, SRF note # 940525-04, (1994)

Fig. 1 Test of the program, for given cavity parameters and ( = 1.

Fig. 2 Five-step shape of the input power pulse keeps reflected power below 4 MW.

Fig. 3. Detail of reflected power.

Fig. 4. Rise of the cavity electric field, (voltage), for the input step function and 5-step pulse.

Input power pulse with a linear ramp increase