ADC Board to Arcturus uC5282 Interface

The ADC board has 4 FIFOs (IDT72V2113 or similar) interfaced to the External Interface Module of the Coldfire 5282 on the Arcturus uC5282 Module.  Analog inputs to the 5282 will also be used to measure temperature and power supply voltages.

The 16bit FIFO data output lines will connect to the 5282 data lines D16 to D31 and be read through the External Interface Module (EIM).  Address lines will not be used in hardware.  Four /CS lines will be used, one for each FIFO, to clock the FIFO.  They will connect to each of the four FIFOs RCLK lines.  CS1, CS2, A21 (CS4) and A22 (CS5) will be the /CS lines used for FIFOs 0, 1, 2, & 3 respectively.  Software will set up an address in CSAR1, 2, 4, & 5 for Chip Select (/CS) to activate.  When the address is read, the /CS will activate and clock the data from the FIFO.

The /OE and the /REN lines for each FIFO will be tied together and connected to PTA0 to PTA3 pins from the 5282.  Each of the four FIFOs can be selected by setting the associated PTA0-3 pin low.  The PTA0-3 pins are dual purpose and can be set for I/O by clearing bit 7 (GPTEN) of the GPTSCR1.  GPTDDR bit 0-3 (DDRT) needs to be high for output.  Data is written to GPTPORT. Bits 0 to 3 of the GPTPORT when low will select FIFOs 0 to 3 respectively.  All pins should be initialized high and only on pin at a time should be low.

The /TA signal will be generated internally by setting bit8 (AA auto-acknowledge) of the appropriate CSCR register high.  Bits 10 to 13 (WS) of this register will be set low to generate 0 wait states.

A word read cycle will take 3 clock cycles at 64MHz.  The 1k work FIFO will be able to be read in 48uS.  All four FIFOs will take about 200uS to read.

The trigger for the ADCs board will be connected to EPORT pin /IRQ1 to interrupt the processor when data collection has finished.  The trigger will come through the CPLD which controls timing.

FLOW

1. Trigger causes FIFO and ADC to reset and collect data.

2. When the FIFOs are full, the CPLD will send a trigger to IRQ1

3. The interrupt request routine reads the FIFO data into processor memory.

A DMA transfer may be set up - need to look into this

3.1 GPTPORT bit 0 is set low to select FIFO 0.

3.2 1024 word reads are done from the port at the /CS1 address

3.3  GPTPORT bit 0 is set high to deselect FIFO 0.

3.4 GPTPORT bit 1 is set low to select FIFO 1.

3.4 1024 word reads are done from the port at the /CS2 address

3.6  GPTPORT bit 1 is set high to deselect FIFO 1.

3.7 GPTPORT bit 2 is set low to select FIFO 2.

3.8 1024 word reads are done from the port at the /CS4 address

3.9  GPTPORT bit 2 is set high to deselect FIFO 2.

3.10 GPTPORT bit 3 is set low to select FIFO 3.

3.11 1024 word reads are done from the port at the /CS5 address

3.12 GPTPORT bit 3 is set high to deselect FIFO 3.

4. Data processing TBD.

5. Wait for host to ask for information.

5282 and FIFO Timing

Processing Capability

Data read from FIFO:

3 clocks / word x 4096 words = 200uS

4096 Reg to mem moves 2 clks / move = 130uS

IQ to Amplitude 2 waveforms of 128 words

128 x			clks

2 x mov	4

Mult		4

3 x mov 	6

Mult		4

Mov		2

Add		2

Mov		2

Sum=2 waveforms x 24clks x 128 words = 6000 clks = 100uS

Average amplitude

128 x			clks

Mov		2

Add		2

Sum=2 waveforms x 4clks x 128 words = 1000clks = 16uS

IQ to Phase 2 waveforms of 128 word arctan lookup

128 x			clks

Mov		2

Cmp	x	2

Goto		2

mov		2

Cmp	y	2

Goto		2

DIV		6

Addptr		2

Mov		2

Sum = 2 waveforms x 22clks x 128 words = 6000 clks = 100uS

Average ( same as above) 16uS

Total Processing Time

4 ADC Read and move data		330uS

2 Channel Average amplitude		120uS

2 Channel Average phase		120uS

Total						570uS

APPENDICES

5282 EIM TIMING

The address bus, write data, TS, and all attribute signals change on the rising edge of CLKOUT. Read data is latched into the MCF5282 on the rising edge of CLKOUT.

13.4.5 Fast Termination Cycles

Two clock cycle transfers are supported on the MCF5282 bus. In most cases, this is impractical to use in a system because the termination must take place in the same half-clock during which TS is asserted. As this is atypical, it is not referred to as the zero-wait-state case but is called the fast-termination case. Fast termination cycles occur when the external device or memory asserts TA less than one clock after TS is asserted.  This means that the MCF5282 samples TA on the rising edge of the second cycle of the bus transfer. Figure 13-9 shows a read cycle with fast termination. Note that fast termination cannot be used with internal termination.

Data is read in on the rising clock edge of S4.

Data setup is 6nS

Data hold is 0nS

At 64MHz CLKOUT cycle time is 15.6nS

The FIFO will be used in a Synchronous (clocked) interface

Speed	7.5	10

Ta (Data Access)	5nS	6.5nS

tens		2.5	3.5

tenh		0.5	0.5

tclk H/L	3.5	4.5