2K samples X 16 bits = 32K bits * 2 = 72Kbits of memory

NetBurner does 2 or 6 cycle writes at 66.355Mhz – 15ns.

Assume 10 cycle write, 150ns/word * 4K words =  615uS.

360 Hz = 2.77mS

Switching to uCDIMM  processor board

3 Trigger Modes

00 – External Trigger

01 – Internal Trigger

10 – CPU Trigger

16 bit register for delay from External Trigger to Dac out

16 bit register for rate of internal trigger. Note: Should be > 2048, the buffer depth.

16 bit register for trigger to SSSB

16 bit register for SSSB width

Voltages to monitor

|  | Source | Type | Range |  |
| --- | --- | --- | --- | --- |
| 0 | SSSB Amp | Temperature |  |  |
| 1 | IQ Modulator | Temperature |  |  |
| 2 | Control Board | Temperature |  |  |
| 3 | SSSB Amp | Bulk Supply | +12V |  |
| 4 | SSSB Amp | Bulk Supply | -12V |  |
| 5 | RF Board | Bulk Supply | +15V |  |
| 6 | Control Board | Bulk Supply | +5V |  |

Temperature Conversion:

ADC input is 0 to 2.5V, Temp input is 20C to 70C so the conversion is

ADC output is 0 to 16383 counts

T (C) = Vout *20 +20

|  | Use |  |  |  |
| --- | --- | --- | --- | --- |
| 00000 0FFE | I Memory |  |  |  |
| 1000 1FFE | Q Memory |  |  |  |
| 2000 | Control Register |  |  |  |
| 2002 | DAC Delay |  |  |  |
| 2004 | SSSB Delay |  |  |  |
| 2006 | SSSB Width |  |  |  |
| 2008 | Ext Trigger Delay |  |  |  |
| 200A | Ext Trigger Width |  |  |  |
| 200C | Int Trigger Rate |  |  |  |
| 2010 | ADC 0 |  |  |  |
| 2012 | ADC 1 |  |  |  |
| 2014 | ADC 2 |  |  |  |
| 2016 | ADC 3 |  |  |  |
| 2018 | ADC 4 |  |  |  |
| 201A | ADC 5 |  |  |  |
| 201C | ADC 6 |  |  |  |
| 201E | ADC 7 |  |  |  |
| 2020 | CPUTrig address |  |  |  |

Control Register (2000)

| Bit |  |  | R/W |  |
| --- | --- | --- | --- | --- |
| [15..08] | Version Number |  | R |  |
| 04 | 119Mhz missing |  | R |  |
| 03 | Ext Trig missing |  | R |  |
| 02 | SSBOverTemp |  | R |  |
| [01..00] | Trigger Mode | 0 => Normal; External Trigger | R/W |  |
|  |  | 1 => Internal Trigger |  |  |
|  |  | 2 => CPU Trigger |  |  |

Connector Assignments

| H1 | SSSB OverTemp |  | Input |  |
| --- | --- | --- | --- | --- |