SPEAR 3 Booster Injection / Extraction Timing

Injection will take place on the “White Circuit” injection gate and 2.24MHz Booster revolution frequency.  The linac will always inject into bucket 0 of the booster.  The injection energy window is ( 2.5 (S, much larger than the 446.3nS injection timing.

After a minimum of 21.6mS of beam damping during the store, the phase will rotate (frequency shift) until bucket 0 is aligned with the desired SPEAR bucket.  The phase rotation will be done at 476.3MHz, before the generation of the booster frequency.  The (11.3kHz shift in booster frequency, 358MHz, will be done by shifting the 476.3MHz by (15.04kHz.  An integral number of 476.3MHz buckets will be shifted for up to (186 buckets or 12.4mS.  The buckets are properly aligned for injection into SPEAR at 320kHz increments.

Extraction will take place at the extraction gate and the 320kHz RF Sync.

Frequency Generator Design Parameters

Dual Channel

Jan 23, 2003

The two channel frequency generator will be used to select buckets in SPEAR 3.  It will drive an I&Q modulator to shift the phase of the booster up to (186 cycles at 476.3MHz.

Each cycle is a 12bit circular buffer of length 1024.  The two circular buffers are sine and cosine data with separate adjustments in offset, phase (buffer start point), and amplitude.

# STATE GENERATOR

Start sequence on trigger.

Read and latch a 9 bit parallel bucket select number.

Delay 34mS – Shift time.

Cycle through 0 to (186 cycles (Selected Bucket).

Delay 34mS – Shift time.

Reverse direction and cycle back through 0 to (186 cycles.

Noise Levels

# 0.1% amplitude variations = 12bit resolution.

# 0.1degree at 15.04kHz modulation = 10bit circular buffer at 15.4MHz.

# 1MHz LPF

# Counter

Clock = 15.4MHz x 4 = 61.6MHz

Max Count = x4(2bit) + Cycle Shift(10bit) + 0 to 186 Bucket Shift(8bit)

+ Cycle timer and Direction(2bit) = 24bit counter

# Interface

# 8 Bit Bucket shift amount 0 to 186

1 Bit Shift Direction

1 Bit TEST – CW frequency shift

1 Bit /RESET

1 Bit TRIGGER IN

# OUTPUT

# BLOCK DIAGRAM

Spear 3 Bucket Select Sine Generator

Actual Unit Built

R. Akre  October 6, 2003

Booster injection trigger to Booster extraction is 35.7mS

DATA_STB and TRIG Functions

The DATA_STB and TRIG are two independent functions.  DATA_STB clocks bucket number data into the input registers on the rising edge.  Data setup time is 50nS and data hold time is 10nS.  The TRIG function, rising edge, clocks the bucket number data from the input register to a secondary register to use during the timing cycle.  Collisions from both DATA_STB and TRIG are not prevented and if the signals are totally random would be expected to occur less than, possibly by an order of magnitude, 1 in 6.4 million DATA_STBs.  The result would be a single bunch ending up in an unknown bucket.

On a trigger (rising edge), Injection Trigger

FDC Q goes high

Data from the input register is clocked into a second register.

The 8 bit count is inverted (255-count) and input to one side 			of a comparator.  Bits 12 to 19 of the state generator go into 			the other side of the comparator.

If TEST is low then CLR on the counters is released, goes high.

The DIR_SHIFT bit is latched and XORed with Q21.  The outputs of the counters used for memory addressing, Q2 to Q12, are connected to one input of an XOR gate.  The second input of the 11 XOR gates are connected together and used to change the direction of the count.

The counters start to count

The memory clock is initially disabled.

After 17mS (1/2 cycle) Q20 goes high and releases the clear on the memory clock D type flip flop.

Once the comparator reaches the preset count the memory clock is enabled and the memory and DAC output sine and cosine waveforms.

At the end of Q20 cycle the memory clock is again disabled for  17mS.

The count direction is then changed on the second half cycle of Q21.

After the 17mS half cycle of Q20, the clear on the memory clock flip-flop is released.

Once again the comparator reaches its preset count and the memory clock is enabled.

The memory starts clocking with the address bits counting in the opposite direction.

At the end of the Q20 cycle the memory clock is disabled.

At the end of the Q21 cycle, ½ cycle of Q22, the Terminal count clears all the counters and the system awaits another trigger.

June 2005 Modifications

The oscillator clock was replaced with a 44.736MHz Oscillator.  The CPLD code was redone to allow the timing shift to occur in the first and last quadrant based on the 4 cycles of Q19.

State Machine Counter

| Bit | Time | Frequency |  |
| --- | --- | --- | --- |
| Q22 | 136mS | 7.4 | Reset Counters / ½ cycle |
| Q21 | 68mS | 14.7 | Change direction / ½ cycle |
| Q20 | 34mS | 29.4 | Disable Mem Clk / ½ cycle |
| Q19 | 17mS | 58.8 | Bucket Cnt 7 |
| 18 | 8.5mS | 118 | Bucket Cnt 6 |
| 17 | 4.25mS | 235 | Bucket Cnt 5 |
| 16 | 2.13mS | 471 | Bucket Cnt 4 |
| 15 | 1.06mS | 941 | Bucket Cnt 3 |
| Q14 | 531uS | 1.88k | Bucket Cnt 2 |
| 13 | 266uS | 3.76k | Bucket Cnt 1 |
| 12 | 133uS | 7.53k | Bucket Cnt 0 / MEM Add 10 |
| 11 | 66.4uS | 15.1k | MEM Add 9 - CYCLE TIME |
| 10 | 33.2uS | 30.1k | MEM Add 8 |
| 9 | 16.6uS | 60.2k | MEM Add 7 |
| 8 | 8.3uS | 120k | MEM Add 6 |
| 7 | 4.15uS | 241k | MEM Add 5 |
| 6 | 2.08uS | 482k | MEM Add 4 |
| 5 | 1.04uS | 964k | MEM Add 3 |
| 4 | 519nS | 1.93M | MEM Add 2 |
| 3 | 259nS | 3.86M | MEM Add 1 |
| 2 | 130nS | 7.71M | MEM Add 0 |
| 1 | 64.8nS | 15.4M | Memory / DAC Clock |
| 0 | 32.4nS | 30.8M | DAC Clock |
| -1 | 16.2nS | 61.7M | System Clock |

Bits 0 & 1 are used to derive memory and DAC clocks.

Bits 2 to 12 are used for the memory address – 11 bits

Bits 12 to 19 are used to count cycles up to 255 with 8 bit 					comparator.

Bit 20 is used to change direction for the cycle counting

Bit 21 is used to terminate the memory clock.

SINE GENERATOR PCB P3

D-Connector Signals

REMOTE CONTROL

Pin	Discription

1	data_stb	Data Strobe to clock in 9 bit number control

2	Bit 0		Bit 0 of 9 bit bucket number control

3	Bit 1		Bit 1 of 9 bit bucket number control

4	Bit 2		Bit 2 of 9 bit bucket number control

5	Bit 3		Bit 3 of 9 bit bucket number control

6	Bit 4		Bit 4 of 9 bit bucket number control

7	Bit 5		Bit 5 of 9 bit bucket number control

8	Bit 6		Bit 6 of 9 bit bucket number control

9	Bit 7		Bit 7 of 9 bit bucket number control

10	Dir_Shift	Direction of bucket shift, bit 9, control

11	Spare	NC

12	Chng_Dir	Local Change direction setting monitor

13	Test		Local Test switch monitor

14	Ground

15	Ground

16	Ground

17	Ground

18	Ground

19	Ground

20	Ground

21	Ground

22	Ground

23	Ground

24	Ground

25	Ground

SINE GENERATOR PCB P2

D-Connector Signals

Front Panel Monitor/Control

Pin	Discription

1	data_stb	Data Strobe to clock in 9 bit number monitor

2	Bit 0		Bit 0 of 9 bit bucket number monitor

3	Bit 1		Bit 1 of 9 bit bucket number monitor

4	Bit 2		Bit 2 of 9 bit bucket number monitor

5	Bit 3		Bit 3 of 9 bit bucket number monitor

6	Bit 4		Bit 4 of 9 bit bucket number monitor

7	Bit 5		Bit 5 of 9 bit bucket number monitor

8	Bit 6		Bit 6 of 9 bit bucket number monitor

9	Bit 7		Bit 7 of 9 bit bucket number monitor

10	Dir_Shift	Direction of bucket shift, bit 9, monitor

11	Chng_Dir	Local Change direction control input

12	Test 		Local Test switch control input

13	Trig_Out	Trigger present output monitor

14	Ground

15	Ground

16	Ground

17	Ground

18	Ground

19	Ground

20	Ground

21	Ground

22	Ground

23	Ground

24	Ground

25	Ground

SINE GENERATOR PCB P1

D-Connector Signals

JTAG PROGRAM INTERFACE

Pin	Discription

1	NC

2	TDI	Data in

3	TCK Clock

4	TMS

5	NC

6	NC

7	NC

8	pullup and 68ohm to 11 & 12

9	NC

10	NC

11	12 68ohm to 8

12	11 68ohm to 8

13	TDO Data out

14	NC

15	NC

16	NC

17	NC

18	Ground

19	Ground

20	Ground

21	Ground

22	Ground

23	Ground

24	Ground

25	Ground

CHASSIS REAR PANEL SIGNALS

MALE CONNECTOR ON CHASSIS

25pin D-Connector

PIN 	Functions

1 	DATA CLK (rising edge)*

2 	Bit0

3 	Bit1

4 	Bit2

5 	Bit3

6 	Bit4

7  	Bit5

8  	Bit6

9  	Bit7

10  	Bit8

11  	NC

12  	Direction Monitor TTL out

13  	Test Monitor TTL out

14	Ground

15	Ground

16	Ground

17	Ground

18	Ground

19	Ground

20	Ground

21	Ground

22	Ground

23	Ground

24	Ground

25	Ground

*Data setup time to CLK 50nS

Data hold time from CLK 10nS

Bit0 to Bit8 are pulled to +%VDC with 2.2k ohms each

DISPLAY PROM

Control Card Input to Bucket Number Translation

0 to 254 => 1 to 255			Bucket Num = Input +1

255, 511 => 0			Bucket Num = 0 for Input = 255,511

256 to 510 => 371 to 117 		Bucket Num = 627 – Input

Decimal to 7 Segment Display

Common Anode - Low is on.

|  | dp | e | f | a | b | g | e | d | ## |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 84h |
| 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | F5h |
| 2 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | A2h |
| 3 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | E0h |
| 4 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | D1h |
| 5 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | C8h |
| 6 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 88h |
| 7 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | E5h |
| 8 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 80h |
| 9 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | C1h |

Decimal to inverted 7 segment display.

State Generator Timing - not updated to reflect June 2005 modification

Does not show June 2007 Modification - See diagram at end of document.