## Slide 1: Pulse Shaping with MIIPS
SASS 8/22/2012
David Nicholson

## Slide 2: Outline
Pulse shaping introduction
MIIPS
  MATLAB Simulations
  Actual implementation

## Slide 3: Laser pulses can be defined in the time or frequency domains
Electric field of pulse is equivalently defined in both
  Time:
  Freq.:
Typical fourier transform properties apply

## Slide 4: The spectral phase components determine the temporal structure of pulse
Constructive and destructive interference determines temporal profile
As pulse propagates through air and optics, dispersion affects the temporal structure

## Slide 5: 2nd Order Phase

## Slide 6: 3rd Order Phase

## Slide 7: There are many methods to measure the temporal profile of fs pulses.
FROG
  Split beam in two
  Cross in SHG crystal and scan time delay
  Phase retrieval problem
SPIDER
  Split beam in three
  Chirp one pulse and cross three in SFG crystal

## Slide 8: The 4-f shaper allows the adjustment of spectral phase components.
Once you have measured the phase, a simple way to correct it, or apply any phase is the 4-f shaper
Spectral components modulated in fourier plane by SLM

## Slide 9: MIIPS allows for pulse characterization and shaping in a single 4-f device.
Takes advantage of SHG sensitivity to phase profile of input pulse
Place SHG crystal and spectrometer anywhere downstream of 4-f shaper to measure and correct phase at the point
Spectrometer
SHG Crystal

## Slide 10: MIIPS leverages SHG’s dependence on the spectral phase profile.

## Slide 11: MIIPS leverages SHG’s dependence on the spectral phase profile.

## Slide 12: MIIPS leverages SHG’s dependence on the spectral phase profile.

## Slide 13: MIIPS leverages NL signals to measure the input pulse’s phase profile.
Input phase is unknown
Apply reference phase modulation with variable parameter, watch SHG
For each step in parameter variation, maximum SHG signal occurs when curvature of total phase is 0.
Construct 2nd derivative, double integrate to find phase
Apply inverse of phase to correct on SLM

## Slide 14: MIIPS iterates on this procedure to find the correct phase to apply.
Apply reference phase on top of unknown phase,
scan the δ parameter.

## Slide 15: MIIPS iterates on this procedure to find the correct phase to apply.
The SHG signals are arranged to give the MIIPS trace.
Each column is a SHG spectrum reading.

## Slide 16: MIIPS iterates on this procedure to find the correct phase to apply.
At each frequency, the peak signal is taken to give
From this, is generated as:

## Slide 17: MIIPS iterates on this procedure to find the correct phase to apply.
Knowing that , we integrate to find:

## Slide 18: MIIPS iterates on this procedure to find the correct phase to apply.
Now start the next iteration, by reapplying the sin modulation.

## Slide 19: MIIPS iterates on this procedure to find the correct phase to apply.
The SHG signals are arranged to give the MIIPS trace.
Each column is a SHG spectrum reading.

## Slide 20: MIIPS iterates on this procedure to find the correct phase to apply.
At each frequency, the peak signal is taken to give
From this, is generated as:

## Slide 21: MIIPS iterates on this procedure to find the correct phase to apply.
Knowing that , we integrate to find:
Red curve is correction from this iteration, blue curve is total correction from all iterations

## Slide 22: MIIPS iterates on this procedure to find the correct phase to apply.
Now start the next iteration, by reapplying the sin modulation.

## Slide 23: MIIPS iterates on this procedure to find the correct phase to apply.
The SHG signals are arranged to give the MIIPS trace.
Each column is a SHG spectrum reading.

## Slide 24: MIIPS iterates on this procedure to find the correct phase to apply.

## Slide 25: MIIPS iterates on this procedure to find the correct phase to apply.

## Slide 26: MIIPS iterates on this procedure to find the correct phase to apply.

## Slide 27: MATLAB simulations demonstrate MIIPS ability to correct unknown phase profiles
MIIPS trace, sin wave scanned over 4π
Time reconstruction of pulse.
  Solid red = TL pulse
  Dashed red = initial pulse
  Blue = pulse after current iteration
Phase profile of pulse
  Red = Initial phase profile of pulse
  Blue = MIIPS determined phase profile after each iteration

## Slide 28: A MIIPS based shaper was built in one of David Reis’s building 40 labs.
Actual setup

## Slide 29: A MIIPS based shaper was built in one of David Reis’s building 40 lab.
Shaping done between oscillator and regen amplifier
  Phase profile maintained through amplifier
SLM is CRi, dual mask 128 pixels
Lens is 6” achromat
Grating is 300 l/mm
Coherent Evolution Regen Amp
SLM
Femtosource Synergy Ti:Sapph Oscillator

## Slide 30: A LabVIEW VI was programmed to talk with instruments and do MIIPS

## Slide 31: The setup was used to compress the oscillator pulse.
SHG spectrum from OO USB2000
Temporal profile measured with A.P.E. SPIDER
  Dotted red = TL pulse
  Blue = temporal profile after each iteration (iteration 0 is pulse with 0 phase applied on SLM)
Spectrum measured with SPIDER
  Slight positive quadratic phase from path difference between MIIPS SHG and SPIDER.
  Higher order negative phase at wings likely due to low SPIDER signal

## Slide 32: There is still room for improvement and work to do.
Switch from lens-based 4f shaper to all reflective
Improve calibration routines for determining applied phase
Increase routine speed
More options in VI
Route the shaped pulse through the Regen amplifier

## Slide 33: There are plans to use the pulse shaper for HHG experiments.
SLM allows phase and amplitude shaping
Plan to explore pulse bandwidth and phase profile parameter space to see effect on HHG signals.
Next gen FELs may be HHG-seeded
  We hope to gain control over spectral properties of HHG
    Linewidth of each harmonic, etc.

## Slide 34: Bibliography
V. Lozovoy, I. Pastirk, & M. Dantus. Multiphoton intrapulse interference. IV. Ultrahshort laser pulse spectral phase characterization and compensation. Opt Lett 29, 2004.
I. Pastirk, M. Dantus, et al. No loss spectral phase correction and arbitrary phase shaping of regeneratively amplified femtosecond pulses using MIIPS. Opt Exp 14, 2006.
J. Vaughan. Ultrafast Pulse Shaping. Chapter 13, Ultrafast Optics. (via http://frog.gatech.edu/prose.html)
R. Trebino, et al. Frequency-resolved optical gating with the use of second-harmonic generation. JOSA B 11, 1994.
I. Walmsley, et al. Characterization of sub-6-fs optical pulses with spectral phase interferometry for direct electric-field reconstruction. Opt Lett 24, 1999.